## Slide 1
30-01-2014
Dept. Electrical Engineering
University of Cape Town
Presented by:
Dr. Simon Winberg
High Performance Signal and Data Processing Workshop 2014
Integrated view of the Reconfigurable Hardware Interface for computiNg and radiO (RHINO) Project
Radar Remote Sensing research Group (RRSG)

## Slide 2: Where our team is from…
South Africa
University of Cape Town (upper campus)
Some views from Cape Town

## Slide 3
Consider this short scenario...

## Slide 4
“FPGA have sure made possibly many innovations!
If I use one in a new project, are there any particular drawbacks I should be aware of?...”
Developer in industry using Microprocessors / CPUs...

## Slide 5
Drawbacks…
I suppose so: Can takes a while to learn the tools for one thing…
Actually there are quite a few other things too…
My response

## Slide 6: Any Drawbacks?!
Things can get rather… muddy!
Only does the digital part – still need analogue components, user interface, and circuitry that interacts with the outside world.
Has a limited number of IO pins that can connect up with external signals.
Susceptible to EM disturbances, PCB and other components needs to be suitably placed to avoid interfering with functioning of FPGA.
Typically a slower clock than most fast CPUs nowadays (e.g. 100MHz clock speed).
Typically has lots of pins that need to be soldered on, needing small track width and multilayer PCBs
Often can’t achieve full utilization of PLBs
Place & route can take a long time to complete
Limitations of internal interconnects
Here’s just a few
FPGA Firmware a specialized form of development that combines challenges of both s/w and h/w… and then some
Eeek!

## Slide 7
Skills development
Design reuse
Knowledge exchange
Some of the significant difficulties include effective...

## Slide 8
Outline
Intro to RHINO
SDR Objectives for Rhino
Skills development challenges
Integrated view of the parts
Further projects
15%
Conclusion

## Slide 9: The RHINO platform
www.rhinoplatform.org
...
Lower cost than ROACH or BEE platform; but various tradeoffs were made, i.e. smaller FPGA, less memory, etc. than ROACH.
Currently $1750
Schematics are all open and freely available, can rework and refab your own version.
Reconfigurable Hardware Interface for computiNg and radiO (RHINO)
PCB Design S. Scott & A. Langman
Tutorials
Documents
Resources
Updates/News
Links

## Slide 10: Overarching purpose of the RHINO Project
Building skills in application development and R&D using FPGA-based reconfigurable computers
With a focus on firmware / software for…
  Radio astronomy digital backend processing &
  Software Defined Radio (SDR) digital signal processing
Radio astronomy DBE
Wireless Telecomms.
Radar
Reconfigurable computing
skilled
graduates

## Slide 11: Why Rhino?
ROACH
GnuRadio (USRP I,II)
BEE
FLEX
BladeRF
Bitshark
HPSDR (Radio Amaeurs)
WARP (Rise University)
Others
A training platform
Collaborative with MeerKAT
Rhino developed ‘in-house’
Open hardware
Open source
BORPH
Reusable & scalable platform design  Reusable source
+ Objectives:
Aims for KATCP support
Connectivity to GnuRadio
Existing systems
Why Rhino:
USRP
ROACH
RHINO

## Slide 12: Rhino Architecture
2x 256MB DDR3 SDRAM
2x 128MB DDR2 SDRAM
2x FMC Connectors
2x CX4 (10Gbps Ethernet)
256MB NAND Flash
USB, SD Card, 100Mbps Ethernet, audio and video
(RHINO 1.x has no ADC/DAC, this provided by FMC add-on boards)

## Slide 13: Software Defined Radio (SDR)
Subsystem breakdown of a SDR system
Image based work by Blossom (2004) and Jondral (2005)
Software
Hardware
Just showing the receiver, which is relevant to radio astronomy applications
A radio system with many of its primary functionality (or ‘front-end’ components) implemented in software instead of hardware
Further
Processing
control
FPGA
ARM

## Slide 14: Towards a ‘World’ of SDR potential applications and prototyping
Radio ‘primary functionality’ examples:
  Band selection / tuning
  Frequency keying
  Modulation or demodulation
  Filtering
Software aspect of SDR system in the form:
FPGA firmware
Software on a DSP
Our Focus
Programs running
on PC with sound card
Basic concept of a
Field Programmable Gate Array (FPGA)
Lots of gates (and other devices) that can be re-connected in many ways to create a digital circuit.

## Slide 15
Skills development challenges
Needing to draw on knowledge of a variety of
specialized fields
36%

## Slide 16: Skills required for SDR
Radio communications
theory
EM radiation
Properties of radio waves
Propagation of radio waves
Frequency bands and their characteristics
Band licensing and management
Antenna design
...
Bold items a focus

## Slide 17: Skills required for SDR
Radio communications
theory
H/W interfacing and standards
Power analysis
Interference, shielding
Signal conditioning
Helps to know Circuit design & analysis esp. if doing analogue i/f
Analogue Electronics

## Slide 18: Skills required for SDR
Radio communications
theory
HDL coding (e.g. VHDL or Verilog)
Implement font-end processing, ADCs
High-speed DSP
Changing analogue methods to digital equivalents
Backend processing C / Python / Java etc
Analogue Electronics
I=V/R
P=I2R
Digital Systems
and
Electronics

## Slide 19: Skills required for SDR
I=V/R
P=I2R
Radio communications
theory
Digital Systems
and
Electronics
Analogue Electronics
Reconfigurable Computing Approach to Software Defined Radio

## Slide 20: Towards... Building local knowledge & stimulating & prototyping radio-related systems
A decentralised community of practice (COP) from different universities and organisations
The RHINO platform as a ‘boundary object’* used within the COP
RHINO reconfigurable computer designed to be such a ‘boundary object’ for software defined radio applications
* Star, Susan; Griesemer, James (1989). "Institutional Ecology, 'Translations' and Boundary Objects: Amateurs and Professionals in Berkeley's Museum of Vertebrate Zoology, 1907-39". Social Studies of Science 19 (3): 387–420.

## Slide 21
That brings us to…
Integrated View of
The Rhino Project
54%

## Slide 22: Parts of the Rhino Project
...
Platform Design and System firmware
MiGen & DSL for SDR
Toolchain investigation & benchmarking
RF front-end, internal bus & ADC/DAC Integration
Comms & digital data transport
Training Resources
Application Development / Prototyping
CASPER interface
Brief view on each one and a look at where the project has got to so far
Brief look
at the parts...

## Slide 23: Parts of the Rhino Project
Comms & digital data transport
Platform Design and System firmware
Toolchain investigation & benchmarking
RF front-end & ADC/DAC Integration
Training Resources
Application Development / Prototyping
CASPER interface
MiGen
DSL using
Delite
ROME
MiGen & DSL for SDR
...

## Slide 24: Parts of the Rhino Project
Comms & digital data transport
Platform Design and System firmware
Toolchain investigation & benchmarking
RF front-end & ADC/DAC Integration
Training Resources
Application Development / Prototyping
CASPER interface
MiGen
DSL using
Delite
ROME
MiGen & DSL for SDR
MiGen
DSL using Delite
Block diagram of design chain
SBT code
L. Mohapi
S. Katz
Rhino Object Modelling Environment (ROME)

## Slide 25: SDR-DSL
Development of a text-based Domain Specific Language (DSL) for Software Defined Radio (SDR) - Referred to as SDR-DSL
Project by: Lerato Mohapi
Building on support of a DSL development tool such as the Delite framework developed at the Pervasive Parallelism Lab.
(OptiSDR)

## Slide 26: MiGen: Milkymist Generator collaboration with M-Labs
Migen innovation and developers:
  Sebastien Bourdeauducq and Alan Langman
  Initially aimed for Milkymist platform by M-Labs, port to RHINO
What is Migen?
  A Python-based tool aimed to automate the VLSI design process
  Approaching the challenges of HDL coding from a different perspective
How does it differ to MyHDL?
MyHDL = A hardware description language based on Python
MiGen = A Python library to generate HDL (Verilog)
http://milkymist.org/3/

## Slide 27: MiGen collaboration with M-Labs
Operation of Migen
  Python acts as a ‘Meta-Language’ (i.e. A language to describe a language)
  Uses methods for generating logic (metaprogramming) through "generate" statements.
  Replaces the event-driven paradigm with the notions of combinatorial and synchronous statements
  Allows design's logic to be constructed from a Python program: This enables hardware designers to take advantage of the richness of the Python language: object oriented programming; function parameters; generators; operator overloading; libraries, etc.... All helping to build well organized, reusable and elegant designs.
Snippet of MiGen code

## Slide 28: Parts of the Rhino Project
MiGen & DSL for SDR
Comms & digital data transport
Platform Design and System firmware
Toolchain investigation & benchmarking
RF front-end & ADC/DAC Integration
Training Resources
Application Development / Prototyping
GPMC
Interface
block
CASPER interface
A. van der Byl & W. New
CASPER toolchain and Simulink modelling system
Generated HDL ...
Interface
configuration

## Slide 29: Parts of the Rhino Project
CASPER interface
MiGen & DSL for SDR
Comms & digital data transport
Platform Design and System firmware
RF front-end & ADC/DAC Integration
Training Resources
Application Development / Prototyping
Toolchain investigation & benchmarking
Evaluating current elec design tools
Supporting scripts and applications
Comparison of developer effort
* Image source
“Taming the RHINO: towards a simplified design tool-chain for the RHINO platform”
Khobatha Setetemela
74%

## Slide 30: Taming the Rhino: Towards a simplified tool-chain for the RHINO platform
Specifications: done visually using signal processing graphs
Functional verification using MyHDL and simulator (Xilinx ISim) to test specifications
Software/Hardware partitioning
  Implementation of HDL and
  CPU-based signal processing functions
Compiling HDL to generate bitfile for FPGA, and compile code for the CPU(s). (This done by BORPH support tools)
Generate BORPH files (i.e. config data to be loaded into BORPH running on the ARM processor), and generation of a GNU Radio interface block.
Deployment and running on hardware.
= manual operations
= automated operation
Project by: Khobatha Setetemela (Msc student)
Details presented tomorrow

## Slide 31: Parts of the Rhino Project
Platform Design and System firmware
MiGen & DSL for SDR
Toolchain investigation & benchmarking
RF front-end & ADC/DAC Integration
Comms & digital data transport
Training Resources
Application Development / Prototyping
CASPER interface
RF front-end, internal bus & ADC/DAC Integration
4DSP FMC105
Digilent Pmods
24-channel MIMO
channelizer
M. Bridges;
focus for new MSc students in 2014
ADC/ ADC HDL interface block

## Slide 32: Putting The Rrrr in RHINO
Developing an open source Architecture for FPGA based Digital Radio.
A set of Gate-ware cores and controller.
Designed to allow software based configuration.
Matthew Bridges | Dept. Electrical Engineering | University of Cape Town

## Slide 33: Parts of the Rhino Project
Platform Design and System firmware
MiGen & DSL for SDR
Toolchain investigation & benchmarking
RF front-end & ADC/DAC Integration
Training Resources
Application Development / Prototyping
CASPER interface
ARM apps
BORPH
RACCMS
Comms & digital data transport
RHINO ARM Cluster Control Management System (RACCMS)
V. Valerie Chiriser
10GB Eth interfacing and performance testing
84%

## Slide 34: RACCMS1 Functional Diagram
...
ARM-PC Cluster Server-Client App
Communication Protocol between the two
GUI RACCMS uses to display outputs
Creates standard for developing registers accessible from ARM to FPGA through GPMC interface
BORPH Linux Driver
Translates network packets into relevant function calls using a lookup table
Created using .sym file when .bof file is generated
Enables C-based code to control RHINO cluster
1 RHINO ARM Cluster Control Management System
by: Valerie Chiriseri (Msc student)

## Slide 35: Building on from RHINO
RF front-end, internal bus & ADC/DAC Integration
MiGen & DSL for SDR
Toolchain investigation & benchmarking
RF front-end & ADC/DAC Integration
Comms & digital data transport
Training Resources
Application Development / Prototyping
CASPER interface
Brief view on each one and a look at where the project has got to so far
White RHINO
RHINO radar
Platform Design and System firmware
White RHINO platform for whitespaces radio application development, spectrum monitoring, commications, radar, etc.
RHINO Radar using RHINO platform to develop radar systems

## Slide 36: White-RHINO
By: Ojonav Hazarika
(Main supervisor: A Mishra)
Much Un-Used spectrum!
Called ‘Whitespaces’ …
e.g. Transition from Analog to Digital TV freed many channels, these are ‘TV whitespaces’
In 2008, FCC was first organization to make TV Band spectrum avail to unlicensed users.
Sharing of Spectrum done by either spectrum sensing or a database management system.
AIM: develop a hardware platform which can operate as Whitespace Communication node with radar detection as its commensal operation.
Applications ideas: communications, ATC, border monitoring, cognitive radio prototyping

## Slide 37: Prototyping SDR Applications on a Reconfigurable Computer (RC*)
Plans for sample radio applications, e.g. undergrad projects:
  Wireless router
  WiMAX receiver
  FM radio
  Television
  Radio direction finder
  Spectrum analyzer
  Two-way radio with voice disguiser
  Radar (e.g. speed sensor)
Some electronic products that can be emulated using a RHINO platform
Some benefits of reconf. computing:
Quicker prototypes
Hardware reuse
Faster infrastructure upgrades

## Slide 38: Conclusions
The various parts of the Rhino project are taking shape
Combination of Xilinx ISE and BORPH works, but more tool support, esp. For prototyping, e.g. Effective use of MiGen and a specialized DSL, could make things quicker and easier.
Main focus for now needs to be on more firmware libraries, signal sampling, and integration with existing HDL processing modules
100%

## Slide 39: Acknowledgements
SKA MeerKAT (Karoo Array Telescope) for funding HPC training and the Rhino platform
Xilinx donation of electronic components and software tools
Texas Instruments for donation of development resources and hardware

## Slide 40
Thank you!

## Slide 41: Any Questions?
110%

## Slide 42
Extra Slides

## Slide 43
Rhino v1.0 schematic