## Slide 1: Development of FARICH technique for the Super Charm-Tau Factory project.
Alexander Barnyakov
on behalf of BINP PID-group of SCT-collaboration
Budker Institute of Nuclear Physics, Novosibirsk, Russia
SCTF project overview
PID system
  FARICH technique progress
  FARICH with dual aerogel radiator concept
Summary
4–8 September 2023
CTICC, Cape Town, South Africa

## Slide 2: The SCT experiment
Super charm-tau factory is 𝑒+𝑒− collider, dedicated to precision study of properties of charm-quark, -lepton, study of strong interactions, search of BSM physics
  Beam energy from 1.5 (1.0) to 3.5 GeV
  Luminosity
  Longitudinal polarization of the beams
Experiments will be conducted using state-of- the-art general purpose detector
  Tracking (including low )
  Calorimetry (high resolution, fast, sep. )
  PID system:
    – separation up to 3.5 GeV/c
    – separation up to 1.5 GeV/c
3
5 м
CDR
ctd.inp.nsk.su

## Slide 3: The SCT energy range
A one-year dataset
, | Events recorded
 | Events recorded
Threshold production of nonrelativistic particles provides best conditions for their comprehensive study
Notes: Супер c-tau фабрика может работать в диапазоне энергий от 2 до 5 ГэВ. На графике показаны частицы, которые могут быть рождены а этом диапазоне энергий.
Первая интересна точка – это чармоний J/psi. Дальше идут пороги рождения пар тау лептонов, D мезонов, Ds мезонов, очарованных барионов, а также серии резонансов psi.
В таблице показаны ожидаемые наборы данных, которые можно получить за год работы Супер c-tau фабрики"Место для уравнения."

## Slide 4: SCT Physics in a nutshell
Measurement of the strong phases of decay amplitudes
Measurement of absolute branching fractions
Searches for rare and forbidden decays of the charm quark
violation in charm
…
charm
tau
QCD
Physics of highly-excited quarkonium
Molecular states
Baryon interaction at threshold
Search for glueballs in decays of and
…
Input for meson studies at LHC and Belle II
Precision measurement of the lepton properties
Michel parameters, tests of lepton universality
Precision measurement of hadronic decays
Search for and T violation in decays
…
QCD, , . Test of the electroweak model, searches for non-standard contributions
Test of the electroweak sector of the SM

## Slide 5
SCT
SUSY,
Charged Higgs
Charm mixing
CKM
CKM
Charged Higgs
CPV in charm
Absolute branching fractions
Quantum correlated
Neutral particles in the final state
Only charged particles in the final state
mixing and lifetime
mixing and lifetime
lifetime
CPV in
Dark matter
LFU
New CPV
LFU
Charm spectroscopy
Charged Higgs
Clear BSM
Clear BSM
Model-independent
Polarized beam

## Slide 6: Detector concept
Momentum resolution at
Very symmetric and hermetic
Able to detect soft tracks ()
  Inner tracker should be able to handle 104 tracks/cm2s
Very good PID:
  up to 3.5 GeV/c, e.g. for mixing
  up to , e.g. for search
  better than 7% for PID below 0.6 GeV/c
Able to detect from 10 MeV to 3.5 GeV, good separation
  Calorimeter energy resolution at 1 GeV
  Calorimeter time resolution ns
Efficient “soft” trigger Ability to operate at high luminosity, up to at

## Slide 7: LFV with tau
ISR photon background [arXiv:1206.1909 [hep-ex]]
LU precise tests with D-mesons
Requires excellent separation from 0.2 to 1.0 GeV/c
to suppress background and so on.
Allowed in several BSM scenario, including SUSY, leptoquarks, technicolor, and extended Higgs models
– reachable upper limit at SCT for the branching of
Requires excellent separation from 0.5 to 1.5 GeV/c to suppress background
Requirements for µ/π–separation from physics program

## Slide 8: FARICH technique
T.Iijima et al., NIM A548 (2005) 383 and A.Yu.Barnyakov et al., NIM A553 (2005) 70
n=1.030 6.0mm
n=1.027 6.3mm
n=1.024 6.7mm
n=1.022 7.0mm
The first 4-layer monolithic sample
Increase Npe due thickness increase without σΘc degradation
2004÷2005
Excellent PID capability were shown at CERN beam test in 2012
A.Yu. Barnyakov, et al., NIM A 732 (2013) 352
The Belle II (ARICH) is the first application of the method
2017
Two layer ARICH-Belle II (n=1.045|2 cm + n=1.055|2 cm) provides exccelent π/K – separation up to 4 GeV/c
Four layer FARICH (thicktotal =3.5 cm & nmax=1.05) is able to provide exccelent ()
    π/K – separation up to 6 GeV/c
    µ/π – separation up to 1.5 GeV/c
Notes: Идея ФАРИЧ появилась в 2004 г.
Точность измерения черенковского угла связана с точностью измерения скорости, а значит с качеством разделения частиц.

## Slide 9
GEM
MaPMT H12700 (Hamamatsu)
with mask 3х3 mm2
2 aerogel pcs
230x230x35 mm
The largest focusing aerogel samples produced in 2022
Refractive index profile is measured with help of didgital X-ray setup at the BINP.
Single photon Cherenkov angle resolution is investigated with relativistic electrons at BINP beam test facilities ”Extracted beams of VEPP-4M complex”.

## Slide 10
FARICH beam test 2023 results
Pixel 6x6 mm
Geom.Eff. ~ 80%
Pixel 3x3 mm
Geom.Eff. ~ 20%

## Slide 11: TBeam results consideration
Aerogel: 20+20 mm (Chiba Univ.)
n(400nm): 1.045 +1.055
Pixel: 5x5 mm
4-layers (Novosibirsk) –>
1.039 ÷ 1.046
6x6 mm
–
–
3x3 mm
4-layers (ideal profile)
1.041 ÷ 1.050
3x3 mm
PTEP 2016, 033H01
Belle II
Simulation
TBeam
Geom.Eff. ~ 80%
Geom.Eff. ~ 20%
SPE resolution ~7÷8 𝑚𝑟𝑎𝑑 is able to provide:
π/K @ 8.0 GeV/c if () and π/K @ 6.0 GeV/c if ()
µ/π @ 1.5 GeV/c if () and µ/π @ 1.3 GeV/c if ()
Geom.Eff. ~ 90%
Dimensions of focusing aerogels 23x23x3.5 cm allow us to design the full-scale FARICH systems for the future particle physis experiments.

## Slide 12: PID options for – separation
  up to 0.6 GeV/c
  up to 0.9 GeV/c
Focusing Aerogel RICH (FARICH)
(4 layer @ =1.05) from 0.5 to 6 GeV/c
ASHIPH@SiPM (n1=1.03 and n2=1.015) from 0.6 to 3.5 GeV/c
A.Yu. Barnyakov, et al., NIM A 732 (2013) 35
Parametric simulation
A.Yu. Barnyakov et al 2020 JINST 15 C04032
EPJ Web of Conferences 212, 01012 (2019),
A.Yu. Barnyakov et al 2020 JINST 15 C04032

## Slide 13: PID options for µ – separation
  up to 0.15 GeV/c
  up to 0.25 GeV/c
TOF with 100 ps up to 0.2 GeV/c, e.g. Chernkov light from entrance window of MCP-PMT
FARICH (4-layer, =1.05) from 0.5 to 1.5 GeV/c
0.1 1 10
A.Yu.Barnyakov et al., NIMA 1039 (2022) 167044
Results of parametric simulation tuned with results of beam test :
– SPR= 1.63 mm
– SPR= 1.36 mm
FARICH with dual aerogel radiator is proposed
to extend down µ – separation from 0.5 to 0.2 GeV/c

## Slide 14: RICH with dual radiators is not very new idea!
Liquid + Gas:
  RICH – DELPHI
  CRID – SLD
    C6F12(n=1.278@190nm) + C5F10(n=1.00174@190nm)
Aerogel + Gas:
  HERMES
  RICH1 – LHCb
    Aer.(n=1.03@400nm) + C4F10(n=1.00137@400nm)
Aerogel + Crystal:
  RICH+ToF – SuperB:
    Aer.(n=1.05@400nm) + Quartz (n=1.47@400nm)
  FARICH – SuperB:
    3-layer aer. nmax=1.07@400nm + NaF (n=1.33@400nm)
Aerogel + Aerogel:
  FARICH – SCTF:
    4-layer aer. nmax=1.05@400nm + aer (n=1.12@400nm)
P=2 GeV/c
Aerogel is material with easy tunnable refractive index!

## Slide 15: Beam tests results of FARICH with dual radiator
GEM2
GEM3
GEM1
GEM1–GEM2
GEM1–GEM2–GEM3
Photon detector
ZrO2 aerogel
ZrO2–SiO2 aerogel:
Thickness 12 mm & ø20 mm;
Lsc(400nm)=21±0.5 mm;
4-layer SiO2 aerogel:
100x100x35 mm;
Lsc(400nm)=37±0.3 mm;
Photon detector
4 MaPMT H12700 (Hamamatsu);
256 pixels with 3x3 mm size;

## Slide 16: µ/π-separation via G4 simulation
FARICH: "ideal” profile
FARICH (“ideal”)+ZrO2–aer. (=1.12/12 mm)

## Slide 17: FARICH system concept for the SCTF
275 tiles 200x202x35 in barrel part
2x55 trapezoidal tiles in end caps:
2x12 – inner radius
2x18 – medium radius
2x25 – outer radius
Aerogel layout
Proximity focusing RICH
4-layer focusing aerogel
  nmax = 1.05 (1.07?), total thickness 35 mm
21 m2 – total area of photon detectors
  • SiPMs – barrel part (16 m2)
  • MCP-PMT – endcap parts (4 m2)
~106 pixels 3х3 mm2 with pitch 4 mm
SHAPE |  | Aerogel size, mm |  |  | 
 |  | 200 | 100 | 75 | 50
Parallelepiped | 6 | 0.86 | 0.74 | 0.62 | 0.5
Trapezoidal | 1 | 0.96 | 0.94 | 0.92 | 0.9
SHAPE |  | Aerogel size, mm |  |  | 
 |  | 200 | 100 | 75 | 50
Parallelepiped | 6 | 0.86 | 0.74 | 0.62 | 0.5
Trapezoidal | 1 | 0.96 | 0.94 | 0.92 | 0.9
GEANT4 simulation
of edge effects
Notes: Идея ФАРИЧ появилась в 2004 г.
Точность измерения черенковского угла связана с точностью измерения скорости, а значит с качеством разделения частиц.

## Slide 18: Summary
In 2020-2023 the essential progress in FARICH technique development was achieved in Novosibirsk:
  The 4-layer focusing aerogel sample with 20x20x3.5 cm size were produced for the first time in the world –> the possibility to create full-scale systems based on 4-layer focusing aerogel Cherenkov radiators was demonstrated
  The measured SPR (~7 mrad) of FARICH based on 4-layer focusing aerogel is in good agreement with simulation and expectation
  Recent progress in high opticaly dense aerogel production with help of ZrO2 dope allows us to consider new design of FARICH detector with dual aerogel radiator which able to provide exccelent µ/π – separation from 0.2 up to 1.5 GeV/c
For further progress of the FARICH option the development of position-sensetive photon detectors and compatible R/O electronics are highly required

## Slide 19: Back up slides

## Slide 20: Photon detector options
SiPM arrays
There are several manufacturer in the world.
It is required to develop and produce special R/O electronics and cooling system to operate with SiPMs in detector conditions
MCP-PMT
There are several manufacturers in the world.
PDE is not so high, it is limited by photoelectron collection efficiency (~60%) and geometrical efficiency is worse than for SiPM option. Severl vendors suggest MCP-PMT with CE=90%
There is no such a big problem with intrinsic noise rejecion in comparison with SiPM option
Specialised R/O elctronics is already developed for other experiments and could be adopted for the SPD experiment requirements
HAPD
Due to axial magnetic field the SiPM is only one possible candidate for the cylindrical part of the FARICH system!!!
For the endacp regions there are three options of photon detectors.
Only Hamamtsu produced such devices for the Belle II experiment and now it doesn’t produced anymore!
Expected PDE of such devices will less than for SiPM option but signficantly (1.5 times) higher than for MCP-PMT option.
Expected gain is about
Development of specialised R/O elctronics is needed. It is possible to adopt some Belle II ARICH system expirience.
The S/N-ratio is about 1000, it means that only thermostabilization system to operate at the room temperature will enough for this option.
59 mm
Planacon XP85112
8x8 pixels with 6x6 mm
Cost: 15
KETEK PA3325-WB-0808
(BroadCom, USA)
26.8 mm
73 mm

## Slide 21: R/O electronics cost estimation
FPG-TDC (GSI)
TOFPET-II (PetSys)
There are two modern approaches in development of specialised R/O electronics:
– ASIC (Application Specialised Integrated Circuits)
– FPGA (Field Programable Gate Arrays)
The differences in performance, power consumption and costs are not sufficient today!!!
if Nch<1000 (2019)
if Nch≤1000
A system with 100kChannel:
(2020)
A system with 30kChannel (HADES):
(2017)
Power consumption:
15mW/chan (ASIC) + DAQ (FPGA)~60mW/chan
Power consumption: ~55mW/chan

## Slide 22: Advantages of the SCT factory
Threshold production of leptons and charmed hadrons
  Well-defined initial state
  Low multiplicity of particles
  Kinematic constraints
Longitudinal polarization of the electron beam
  Boosted sensitivity to 𝒞𝒫 violation in baryons and leptons
  Measuring the Weinberg angle
Coherent pairs
  Measuring charm mixing and 𝒞𝒫 violation with unique techniques
  Measuring phases of the decay amplitudes
Full event reconstruction
  Superior background suppression
  Measuring absolute branching fraction of charmed hadrons

## Slide 23: Aerogels with high optical density
Sintering approach
ZrO2 addition approach
230 мм
230 мм
n=1.05
n=1.12
n=1.2
n=1.25
n=1.13
The main flaw
of this approach
Lsc(400nm)
Refractive index
The first sample of
SiO2–ZrO2 aerogel
The addition of small amount (0.03÷0.06 mol) of ZrO2 in SiO2 based aerogel alow us to produce highly transperant aerogels with high optical density:
Refractive index up to n=1.12
Rayleigh light scattering length Lsc(400nm) up to 30 mm

## Slide 24: Beam tests with FARICH in 2021-2022 at BINP
GEM2
GEM3
GEM1
GEM1–GEM2
GEM1–GEM2–GEM3
Electrons with E=2 GeV are used
4 MaPMTs (H12700 from Hamamatsu with pixel 6x6 mm) were used with different masks to reduce effective pixel size:
  Ø1 mm to investigate contribution from aerogel itself
  3x3 mm to measure realistic Single Photon Resoulution (SPR)
Three GEMs are used at beamline:
  Two before aerogel sample and one behind
  It alows us to restore Chernekov angle for each detected photon and mitigate multiple scattering affects at beam-line.
Photon detector
ZrO2 aerogel
G N Abramov et al 2014 JINST 9 C08022

## Slide 25: G4 simulation vs beam test results
TBeam results
G4 simulation results
Optical parameters for G4 simultion
PDE for H12700 from data-sheet
Pixel 3x3 mm with pitch 6mm
Focal distance L=172 mm
The main difference between G4sim and TBeam is a photon small angle scattering effect on aerogel surfaces and inside. These effects have not implemented in G4sim yet.

## Slide 26: FARICH system concept for SCTF project
Proximity focusing RICH
4-layer or gradient aerogel radiator nmax = 1.05 (1.07?), 35 mm thickness
21 m2 total photon detector area
  SiPMs in barrel (16 m2)
  MCP PMTs in endcaps (5 m2)
pixels with 4 mm pitch & 3x3 mm2 sensitive area
Main requirements for PID system:
separation up to 3.5 GeV/c
suppression for
Below 0.2 GeV/c separation could be performed with help of tracking system by means dE/dx technique (cluster counting mode) or with ToF technique using Cherenkov light from entrance window of fast photon detectors ()
FARICH with dual radiator was considered to provide separation in momentum range
Variable allows to increase using thicker radiator without compromising
T.Iijima et al., NIM A548 (2005) 383 A.Yu.Barnyakov et al., NIM A553 (2005) 70
n=1.030 6.0mm
n=1.027 6.3mm
n=1.024 6.7mm
n=1.022 7.0mm
First 4-layer aerogel
Focusing Aerogel RICH approach
FARICH system for SCTF project
2012 test beam: µ/π separation >3σ at P=1 GeV/c was demonstrated
A.Yu. Barnyakov, et al., NIM A 732 (2013) 35
Notes: Идея ФАРИЧ появилась в 2004 г.
Точность измерения черенковского угла связана с точностью измерения скорости, а значит с качеством разделения частиц.