## Slide 1
Design and Implementation of the TDAQ System for the JUNO-TAO Detector
Xiaolu Ji
Institute of High Energy Physics, CAS, China
On behalf of the JUNO Collaboration

## Slide 2: Outline
Introduction to JUNO-TAO
TAO TDAQ system design and implementation
  CD trigger
  TVT hardware trigger
  DAQ
Summary

## Slide 3: JUNO-TAO
Taishan Antineutrino Observatory (TAO), a ton-level, high energy resolution LS detector at 30 m from the 4.6 GWth core, a satellite exp. of JUNO.
Measure reactor neutrino spectrum w/ high E resolution
  Model-independent reference spectrum for JUNO
  A benchmark for testing the nuclear database
CDR: 2005.08745
core 1
core 2
TAO

## Slide 4: TAO Detectors & Electronics
Water Tank (WT)
3 tanks, ~100 3” PMTs for each
Top Veto Tracker (TVT)
Plastic scintillator: 160 strips (4 layers)
SiPMs at both ends: 320 tiles, 0.8 m2
Share SiPM readout electronics
250/125 MHz sampling, raw readout dominated by SiPM dark rate
Re-use the 3” PMT electronics of JUNO
Triggerless readout
Central Detector (CD)
2.8 ton Gd-LS
Full coverage of SiPM (10 m2) w/ PDE > 50%
Operate at -50 ℃ (for SiPM dark noise reduction)
Energy resolution <2% resolution @ 1MeV

## Slide 5: TAO TDAQ Highlights
Readout from 3 individual detectors’ electronics
Suppress total bandwidth to < 100 Mbps before storage
TVT
WT
CD
128 Gbps #
~10 Gbps ##
~105 Mbps
# SiPM dark rate: 100Hz/mm2 (conservative)
## 1.5 p.e threshold

## Slide 6: Data Suppression Strategy at TAO TDAQ
Data Stream | Raw Readout | HW trigger | DAQ Data input | SW Trigger | Compres-sion | Data Merge | Storage
CD | 128 Gbps | Y | ~800 Mbps | N | Y | Y | <80 Mbps
WT | ~105 Mbps | N | ~105 Mbps | Y | Y | Y | <10 Mbps
TVT | ~10 Gbps | Y | ~40 Mbps | Y | Y | Y | <1 Mbps
SUM | ~140 Gbps |  | ~1 Gbps |  |  |  | <100 Mbps

## Slide 7: CD trigger TVT hardware trigger DAQ

## Slide 8: CD Trigger System Structure
High-performance
  1GHz hit rate
  128Gbps data processing
Physics trigger mode: multiplicity trigger (nHit)
coincident DCR < 1 Hz if nHit > 170
Support External trigger for LED calibration
Random/periodic trigger for diagnosis
Reliable, flexible, scalable, maintainable…

## Slide 9: Hardware Implementation
mTCA standard: CD Gather Unit (AMC) + CD Gather Unit Rear (RTM)
CD Gather Unit / Central Unit: same hardware, different firmware
High data transmission
Hot-swap capability
Rear I/O
Redundancy available
mTCA crate

## Slide 10: NHit Trigger Logic
nHit sum in slide window ≥ nHit Threshold
Record timestamp, generate trigger
Readout data in the window
nHit trigger logic
CU sum the partitioned nHit
process trigger algorithm
CU(Central Unit)
Each CGU board count local nHit
  parallel processing: 1 RAM for 1 FEC
nHit count method - mapping-based approach
  time stamp  RAM address
  nHit count  RAM data value
CGU(CD Gather Unit)

## Slide 11: Firmware Design and Implementation
CGU
CU

## Slide 12: CD trigger TVT hardware trigger DAQ

## Slide 13: TVT Trigger Definition
stage 0: waveform -> (Q,T) pair @threshold 0
stage 1: coincidence of 2 ends in single strip -> window @threshold 1
Stage 2: coincidence of layers -> window @ multiplicity threshold
stage 0 @ FEC
stage 1 @ trigger board
stage 2 @ DAQ
SiPM DCR: ~50 kHz/mm2 @25℃
Muon rate: ~32 Hz/Strip (strip size: 0.2 x 0.2 m2, muon flux 80 Hz/m2)
Natural radioactivity: ~1 kHz/Strip

## Slide 14: S1 Hardware Trigger Requirements
Bandwidth
  FEC -> trigger system: ~10 Gbps *
  trigger system -> DAQ: ~40 Mbps **
Algorithm: coincidence trigger
  utilize the coincidence in both charge & timing from dual-ends to reject DCR
TVT Trigger Logic Diagram
stage 0 @FEC
stage 1 @TGU
stage 2 @DAQ
*DCR: ~0.22 MHz/channel @1.5 p.e.
**mostly from natural radioactivity

## Slide 15: Hardware Design
TVT trigger system use same hardware board as CD, different firmware
TVT: top veto tracker
TGU: TVT gather unit
FEB: front end board
FEC: front end controller

## Slide 16: Firmware Design and Implementation
Trigger Processing Flow
*ch1、ch2:the channels of a single plastic strip
Logic Diagram

## Slide 17: CD trigger TVT hardware trigger DAQ Design and Implementation

## Slide 18: JUNO/TAO DAQ Architecture Design
JUNO and TAO share same DAQ architecture
  Share data file format and data
  transfer system
  Integrated monitoring
Distributed framework
Plug-in modules design
Distributed Framework
Data Assemblers
Data Storages
Data
Processors
ReadOut
Subsystems
CD
TVT
WT
Compression
Software Trigger
Read Out Plug Modules
Process Algorithm Plug Modules
Data Acquisition Utility Modules
JUNO/TAO DAQ System is divided into Data Flow and Online

## Slide 19: Data Flow Software
Support triggered/triggerless data stream
data assembling by ID or timestamp
Online data processing interface provided
Modular design
Readout Elec.
ROS1
Data Flow
Manager
ROS ready
Data to ROS buffer
Data
Assemblers
Asign DAk
Storage
ROSs
To DAk
Readout Elec.
Data Flow
Release Buffer
Data Storages
Reserved data
Request data
End DA
Data Processors
(Farm)
Asign DPm
Data Storages
Data Compression
Software Trigger
DP
Data Flow
Online event classification

## Slide 20: Online Data Processing
Data Assemblers
Data Processers (Farm)
Storage
Data Processing
Data Storages
Data Flow
Manager
Assigned DP
data
message
Full channel data
Event type
Compressed data
Data Compression
Software Trigger
Online event classification
Provides high-performance real-time online data processing interfaces
Split the data stream based on timestamps – parallel processing
Parallel online processing
  Interface provided
  Customized processing can be integrated
  Algorithm can be provided by different experts
 | DAQ input rate | DAQ output goal (limited by network)
JUNO | 400 Gbps | 500 Mbps
TAO | ~ Gbps | <100Mbps

## Slide 21: Online Software
Online Software: provide various interface and services
Online Software | HTTP Interface |  |  |  | 
 | Online Service | Configuration Service | Run Control Service | Message Service | Process Management Service
 | Message Brokers |  |  |  | 
 | Client Interface | Configuration Interface | Run Control Interface | Message Interface | Process Management Interface
Data Flow Software |  |  |  |  | 
Redis based services
Run in k8s managed containers.
Web based GUI
Detection tool for exception diagnosis

## Slide 22: Online Monitoring System Design
MVC based: modular design - low coupling, reusable, easy to deploy and upgrade

## Slide 23: Online Monitoring for Data Quality
ADC SPE
ADC MEAN
Trigger Rate
ROOT & JSROOT
  Visualization and data analysis tool
  Expert user friendly
DCR monitor
Redis & Prometheus & Grafana
  Complete monitoring and visualization solutions
  Rich variety of charts and dashboards
  Support for viewing history

## Slide 24: Online Monitoring for DAQ Running Status
DAQ working status
  APP, process, system running status…
  Memory and CPU usage of each process
DAQ Data Flow status
  Throughput, process rate, counter, buffer usage..

## Slide 25: DAQ Web GUI
All the monitoring modules will be integrated into DAQ web GUI
– control and monitor remotely
DEMO
Run control
Configuration
Process info
Log message
Data flow monitoring

## Slide 26: TAO TDAQ Current Status
SiPM in cryostat
 FEB prototype
DAQ
FEC/CU/CGU/WR switch 
Major development work completed
  Key modules verified
  Self-developed hardware all ready
Whole chain tests has started
Will be fully ready at end of 2023
GCU – readout electronics
WT prototype with PMTs
DAQ
Joint test with sipm
Joint test with WT 3-inch PMT
DAQ
CGU +CU + WRT
Signal generator
WR switch
CD
TDAQ test
TVT

## Slide 27: Summary
Design and build a pure digital TDAQ system for JUNO-TAO
Trigger algorithms on FPGA + compression strategies on CPU
  Reduce data rate O (100Gbps) -> < 100Mbps
Expected time for TAO be online at 2024
2018
TAO Project Approval
2020
TAO CDR
2021-2022
TAO FDRs
2023
TAO CD prototype
2024
TAO online
Ｔｈａｎｋｓ！