## Slide 1: Low Radioactivity Argon for Dark Matter searches
Topical workshop on “New Horizons in TPCs” – Santiago de Compostela 6-October-20
Roberto Santorelli
CIEMAT – Madrid
(on behalf of the DarkSide Collaboration)
TIPP 2023 – CTICC Cape Town, 06/Sep/2023

## Slide 2
Outline
LAr for Dark Matter direct searches
Ar-39 in atmospheric Ar
Radiopure UG-Ar: extraction and purification
DArT experiment @ LSC
Prospects of the UG-Ar for rare event searches
Conclusions

## Slide 3
LAr: A Dream technology for DM search
Large Exposure (Mass  Time) : 100s tonneyear
Low Energy Threshold : ~10 keV
Event topology : alpha, muon..
Discrimination between Signal and Bkg: > 108
Bkg Rate after cuts : <0.1 evt in the exposure
ArDM @ LSC
JCAP 12 (2018) 011
Scintillation
Pulse Shape
Ionization /
Scintillation
Due to enhanced electron –ion
recombination for NR
Background Interesting Signal

## Slide 4
DarkSide-20k @ LNGS
DS-20k UG @ LNGS
200 ty: 6.3×10-48cm2 (90% C.L., 1 TeV/c2)
< 0.1 bkg in 200×20 ty exposure Background free
365 cm drift
≈650 t Ar in a membrane cryostat (VETO)
50 t (20 t FV) Ar target
21 m2 cryogenic SiPMs
>10 phe/keV in the TPC (S1)
top/bottom planes Gd loaded (1%) acrylic (n- thermalization/capture)

## Slide 5
Large mass (tens to hundreds of tons) and long drift (some meters scale)
Very low thresholds ( keV)
New sensors
Extreme radiopurity
Frontiers

## Slide 6
“Measurement of the specific activity of Ar-39 in natural Argon”
NIM-A 574 (2007) 83–88
β-emitter with 565 keV endpoint, T1/2=269 y (cosmogenic)
Pure beta emitter, no accompanying gamma radiation
17 mBq/m3 in atmosphere
Present in AAr due to the production process (isotopic abundance  8×10-16 g(39Ar)/g(NatAr) )
39Ar in Atmospheric Argon (AAr)
1.01  0.02(stat)  0.08(syst) Bq/kg of NatAr
Pileup problems in multi-ton TPCs!!!

## Slide 7
Radiopure target: Underground Argon (UAr)
International effort underway to procure radiopure argon extracted from underground reservoirs
Argon from underground gas reservoirs  shielded from cosmic rays
Production from natural radioactivity reactions (e.g. (α, n)-induced on 39K) suppressed if the gas is from the mantle (ppb level of U and Th)
1400 ± 200 39Ar depletion factor in UAr with respect to AAr
Phys. Rev. D 93, 081101 (2016)

## Slide 8
Extraction – Purification – Measurement
Three sites to extract, purify and measure the radiopure argon

## Slide 9
Extraction
URANIA project: Production ready for construction in Cortez mine, Colorado. First procurement of 60 ton from the CO2 wells
250 kg/d, 99.99% purity
(120t +25th per 0vbb)

## Slide 10
Purification to the detector grade
350 m height, 31.8 cm inner cryogenic distillation column (Sardinia, Italy)
The tallest ever built of this type
Designed to reduce the isotopic abundance of Ar-39 in UAr
by another factor of 10 per pass
Production rate with ARIA in chemical purification mode (DarkSide-20k): 1ton/day
Production rate with ARIA in isotopic separation mode: several kg d-1
Medical applications (isotope supply)
ARIA project: Ar chemical purification by cryogenic distillation (1t/day)

## Slide 11
ARIA
Top module (Condenser) - 7m
Middle modules -12m
Bottom module (boiler) - 5m
SERUCI-0: short version of the Aria column using only the reboiler, the condenser, and one central module
SERUCI-1: 28 middle modules
Successful nitrogen
distillation run of the SERUCI-0 prototype installed outside the Carbosulcis coal mine
Eur.Phys.J.C 83 (2023) 4, 435
Isotopic ratio 36Ar/40Ar as a function of time.

## Slide 12
ArDM detector:
850 kg active volume (2 t total)
  Cryogenic low rad. PMT arrays (R5912 2×12)
  50 cm passive neutron shield (Poly, 20 ton)
Data taken 2014-2018
UAr radiopurity measurement @LSC:ArDM
Main Lab under mount Tobazo
~850 m rock
~2500 mwe
1400 m2

## Slide 13
OFHC copper vessel with two top pipes.
Two 1 cm2 SiPMs at top and bottom with the electronics integrated.
External acrylic support structure. Cylinder + two SiPM supports.
Internal acrylic cylinder and two disks covered with TPB (200 μg/cm2).
Reflector around SiPMs and between acrylic cylinders.
Act.volume of 1.4 kg: 620 evt/week for UAr (0.73 mBq/kg).

## Slide 14: in ArDM
Signal: 𝛽 decays of 39Ar (ROI ∈ [0,600] keV) with < 10 keV deposited in the veto (minimal veto threshold)
Background: untagged 𝛾 particles mainly from the radioactive decays in the detector materials (+ external)
Background source | Evts/week ROI | Untagged Evts/week ROI
ArDM Cryostat | 3164.4 | 218.3
ArDM PMTs | 1053.0 | 42.8
ArDM supp. structure | 28.5 | 0.6
Lead Belt | 150.5 | 16.2
DArT vessel | 16.6 | 5.4
Arlon SiPM | 40.9 | 23.5
Acrylic | 9.1 | 4.1
External without Pb | 117623.0 | 10020.5
Total without Pb | 122098.9 | 10301.7
External with Pb | 2596.2 | 155.7
Total with lead | 7209.9 | 465.5
Signal 620 evt/week (D.F. 1400)
→ S/B > 1 for UAr

## Slide 15: in ArDM
“Design and construction of a new detector to measure
ultra-low radioactive-isotope contamination of argon”
JINST 15 (2020) 02, P02024.
Monte Carlo
Depletion factor with respect to AAr | Statistical uncertainty [%]
10 | 0.4
100 | 1.3
1400 | 6.7
14000 | 41.1
DS-50
Installation in ArDM by the end of 2023
Commissioning of DArT in ArDM in 2024
Detector fully operative from early 2025
In the long term, DArT will measure on a regular basis the UAr batches received from URANIA/ARIA before their use in DarkSide-20k

## Slide 16: ArDM preparation
13 new cryogenic PMTs (R5912) for the veto
New reflector cage with TPB on the reflector panels
New 6 t inner Pb shield

## Slide 17
Commissioning in a test setup
Independent from ArDM
Control on the filling level performed by Arduino Mega acting on two (In & Out) cryogenic valves.
Automatic filling system
Filling triggered by level meter.
Online monitoring with a webcam on a raspberry.
Remote actuation possible via ssh for emergencies.
Several weeks of data taking in stable conditions

## Slide 18
AAr data in the test setup
Data
𝜷 decay
 decay

## Slide 19
AAr data in the test setup
Preliminary
39Ar rate  1 Hz
assuming a featureless linear bkg
(systematics under study)

## Slide 20
We are considering liquid containers: final choice of specific container still to be made.
The activity of 39Ar induced during extraction, purification and transport on surface, in baseline conditions, is evaluated to be <5% of the UAr activity measured in DarkSide-50 (Astropart.Phys. 152 (2023) 102878), and thus considered acceptable.
Other products in the UAr such as 37Ar and 3H are shown not to be relevant due to short half-life and assumed purification methods.
UAr Transportation

## Slide 21
UAr for rare events searches
Conceptual studies : 3 kt x 10 yr
 100 t produced for DarkSide-20k (starting Q4 of 2024)
We recently signed with the LEGEND Collaboration an agreement for the provision of 25 t of UAr for the LEGEND1000 argon veto, after the DarkSide-20k production (Ar-42 background mitigation).
A lot of interest from other experiments
COHERENT 1 t (CEvNS)
ARGO 300t (dark matter)
DUNE O(10,000) t

## Slide 22
Conclusions
The small Ar-39 contamination does not make feasible to use atmospheric argon in the next generation of Dark Matter search experiments
~1400 depletion demonstrated in UAr: UAr will be key to the physics programs of the future DM direct search with argon
International effort underway to procure radiopure argon extracted from underground reservoirs with three different projects: URANIA, ARIA and DArT
First 2 y production for DS-20k by the end of 2024
A lot of interest from the rare event search community

## Slide 23: Thank you!

## Slide 24
Extraction – Purification – Measurement

## Slide 25
DarkSide-20k @ LNGS
365 cm drift
50 t (20 t FV) low-radioactivity Ar (UAr)
21 m2 cryogenic SiPMs
5 m2 cryogenic SiPMs in the Veto
99 t UAr in total in a Ti vessel
TPC lateral walls + additional top/bottom planes
in Gd loaded (1%) acrylic (n- thermalization/capture)
≈650 t AAr in a membrane cryostat, proto-DUNE like
2 independent cryogenics purification loops
>10 phe/keV in the TPC (S1)
>20 PE/e- (S2)
2 phe/keV in the Veto
cm (xy) and mm (z) pos. res.

## Slide 26
Commissioning in a test setup
Setting the operating conditions of the system
Long terms stability
Characterization of the DAQ
Study of the SiPM optimal operating conditions
Data transfer / processing / storage
Test of the reconstruction/analysis tools
Tuning of the MC
First study of the internal backgrounds
𝜷 decay
 decay
Triplet lifetime 1230 ns
Data