## Slide 1: Design and prototyping of large-scale flex circuits for the ATLAS ITk Pixel detector
Presenter: Steven Welch from Oklahoma State University
On Behalf of the ITk Pixel Collaboration

## Slide 2: ATLAS
25 Meters in diameter
44 Meters Long
7000 tons
The ITk Pixel is only
  ~6 meters long
  1 meter in diameter
700cm
6m
ITk Pixel Detector

## Slide 3: Pixel
L0 Radius is 50mm
L1 Radius 100mm
Radiation is up to 1G Rad TID
~900 serial power chains
~8400 sensors
~26000 data transmission lines running at 1.28Gbps
Plots and Figures: https://atlas.web.cern.ch/Atlas/GROUPS/PHYSICS/PUBNOTES/ATL-PHYS-PUB-2021-024/
Overview Talk: https://indico.tlabs.ac.za/event/112/contributions/2963/
ITk Layout 23-00-03

## Slide 4: Pixel Structures and Services
End Cap Half Rings
Outer Barrel: Inclined Half Rings and Longerons
Inner System End Cap
Inner System Barrel

## Slide 5: Local Support Flavors
L1 Quad Ring
Inclined Half Ring
Longeron
Layer 2,3,4
Notes: Describe a bit more here and talk about radius 50mm to 300mm radius

## Slide 6: Design Philosophy
Our design process attempts to validate design concepts before they are integrated into final designs
Transmission line Validation
  Design
  Simulate
  Fabricate Coupon
  Validate Design
    SI (Signal Integrity) tests, X-Rays, SEM, etc.
This process helps ensure that the expensive and complex designs are right the first time
We do this for every controlled impedance structure
We do something similar for HV structures
We don’t validate LV structures as the are predictable enough.
These validated stack-ups and structures are then used in multiple designs
COMSOL Simulation
Hatched Ground Plane S11 S21
Samtec BDRA on
Transmission Line Coupon
SEM Analysis of VIA
X-Ray of Flex PCB
with BGA
Polar Instruments
Stack-up and VIA Model
Notes: For example if we need a transmission line for a coupled ring for example we design, simulate, build a test coupon, and then validate that structure before we integrate it into a more complex design like a coupled ring.

## Slide 7: Stack-ups
Polar Instruments
Differential Co-planar Stripline
Polar Instruments
Co-planar Microstrip
Polar Instruments
Differential Co-planar Microstrip
Polar Instruments
6-Layer Flex Stack-up
Polar Instruments
2-Layer Flex Stack-up
Notes: We start our simulations with choosing and modeling a stack-up. We then create some preliminary simulations for the controlled impedance structures we need and start communicating with the vendors (3 vendors normally) in Speed Sack, or ADS, Hyperlynx

## Slide 8: Loss Simulations
Polar Instruments
Co-Planer Differential Strip-line
Line Length = 330mm
Rise time = 110ps
Loss @600Mhz = -1.33dB
Loss with roughness (0.35um) = -1.41dB
COMSOL
Co-Planer Differential Micro-strip
hatched ground
Line Length = 50mm
Rise time = 110ps
Loss @600Mhz = -0.3dB
Notes: After the stack-up is validated we can move on to loss simulations. For systems with hatched ground planes we have to use 3D FEAs to calculate loss as most of the tools don’t support loss calculations with hatched ground planes.

## Slide 9: VIA Simulations
Impedance Vs Time
Simulated TDR
(Time Domain Reflectometry)
Loss Vs Frequency
Simulated VNA
(Vector Network Analyzer)
Frequency Domain
VIA Layout
Using ADS
Stack-up
Using ADS
Notes: Lastly we can simulate the VIA structures. ADS and Hyperlynx, System Level Simulations allow you to calculate the loss of the whole system

## Slide 10: System Simulations
Each Block Represents all the components that make up the service type
The Blocks contain models of connectors and transmission lines
We can put together a bunch of these blocks to model the whole system and look at things like loss at a system level

## Slide 11: Test Coupons Testing
This is a sample of a type-0 to PP0 flex PCB
Has a line length of ~80mm
  We predicted loss at 0.006dB/mm
That means coupon should have ~0.5dB of loss
Cables have a loss of about 0.25dB
Connectors have about 0.12dB
Total loss is -1.27dB
0.25*2+0.12*2+0.5 = 1.24
VNA Loss Measurement
VNA Loss TDR Calculated Eye-Diagram
Controlled Impedance Flex Coupon
Connected to VNA

## Slide 12: Prototypes - Large Scale Flex Circuits
Outer Endcap
Half Ring
Outer Barrel
Inclined Half Ring
Outer Barrel
Two Longerons
Notes: What do we mean by large scale, well large from many perspectives physical size, the quantity. Some of these flexes are more than 1m long and in many cases we have thousands of them.

## Slide 13: Prototypes - High Density Data Flexes
Outer Barrel PP0
Inner System Type-0 to PP0 Flex
Inner System
Ring Flex
Outer Endcap
Data PP0
Notes: Another form of large scale comes from the quantity of combined services in a single flex.
These flexes carry up to 50 differential pairs each over a long distance, for a flex PCB anyway. These flexes also carry up to 8A of current and 1000V of sensor bias voltage. All on the same flexes

## Slide 14: Testing Flex PCBs – Radiation Hardness
Typical Flex PCB Adhesives
  None
  Epoxy
  Acrylic
  Teflon (PTFE)
  Polyester
Typical Flex PCB Dielectrics
  Polyimide
  Teflon (PTFE)
  Kevlar
  Vinyl
  PET
IPC-4204 and IPC-4203
  We tend to use:
    IPC-4203/2 – Epoxy Adhesive on one or both sides of polyimide dielectric
    IPC-4204/11 – Copper Clad Adhesive-less Polyimide
There are only a few Materials used in the services
  Known to be Radiation Hard
    Kapton (Pyralux AP)
    Copper
    Liquid Crystal Polymer (LCP) (Connectors)
  Tested
    Epoxy (Thinflex, Pyralux HP, etc.)
    Terra Green (Rings and PP0)
    Low Density Polyethylene (LDPE) (Twin-ax)

## Slide 15: Testing Flex PCBs – TDR (Time Domain Reflectometry)
TDR Testing helps us understand the impedance vs time/distance
The plot shows the impedance along the signal path
We can identify issues in the PCBs and VIAs and where the issues are in the data transmission chain
Can calculate Bit Error Rate and Eye Diagrams
TDR Measurement of Impedance
TDR connected to
Outer Endcap PP0
Ohms
Pico Seconds

## Slide 16: Testing Flex PCBs – VNA (Vector Network Analyzer)
VNA combined with multiplexers allow us to scale the test stand and scan multiple transmission lines
BDRA cables and Low Loss Test fixtures help reduce the loss in the test stand
Easily measure insertion loss, FEXT & NEXT Crosstalk
VNA connected to
Inner System Type-0 to PP0 Flex
VNA Measurement of S11 and S21

## Slide 17: Testing Flex PCBs – BERT (Bit Error Rate Test)
BERT testing allows us to evaluate the performance of the channel or cable plant as an integrated system
Great tool for system testing and design validation
BERT connected to Integrated
Inner System Coupled Ring
BERT test of Integrated
Inner System Coupled Ring

## Slide 18: Testing Flex PCBs – Oscilloscope
The Oscilloscope allows us to measure at the system level
We can use the actual detector components in this kind of test
We can look at the Eye diagram, jitter, and inter-symbol interference at any point in the system
Essential, but not scalable
Great tool for system testing and design validation
Top -Oscilloscope Measurement of Data Through the Coupled Ring Assembly
Left – Test System containing Module, Coupled Ring Assembly and Readout

## Slide 19: Testing Flex PCBs – Connectivity, Resistance, HV
Cirris High Voltage Tester checks for connectivity, resistance, capacitance, and High Voltage (DWV, Dielectric Breakdown, and Insulation Resistance)
Easily scales to production
FLIR Cameras look at temperature and help evaluate current density and power dissipation
High Precision multimeters and high current power supplies evaluate overall resistance
Outer Barrel PP0
Power Distribution Test with FLIR
Inner System Flex on Cirris HV Tester
Notes: This is the tester we use for Connectivity, Resistance and High Voltage Tests.

## Slide 20: Initial integration test
Inner System Integrated
Coupled Ring
Outer End Cap
Integrated Half Ring ->
Outer Barrel
Integrated Inclined Half Ring

## Slide 21: Summary
We have developed a process for design, fabrication, and testing of flex PCBs
Flex PCBs are extremely versatile and have made their way into every subsystem
We have pushed the use case, density, and and size of Flex PCBs as far as we can
The use of Large Scale Flex PCBs has enabled us to substantially increase the capability of our detectors while reducing the size and increasing the data rate of the detectors
Fabricating the PCBs requires careful definition of requirements and proper design techniques
Testing of Large Scale Flex PCBs almost always requires complicated custom test fixtures as well as test systems that can be easily scaled
Essential to the development of high performance detectors
All of the On Detector services are in Pre-Production now.
We expect a Production readiness review in the Spring of 2024

## Slide 22: The End
Questions?
TIPP 2023 @ Cape Town

## Slide 23: Backup Slides

## Slide 24: Collaboration Structure
CERN
LHC
ATLAS
CMS
ETC.
Pixel
LAR
Strips
ETC
Inner System
Outer Barrel
Outer End-cap

## Slide 25: Type-0 Status
All of the prototypes Type-0 services that were delivered to SLAC

## Slide 26: Prototype Integrated Coupled Ring in the cold box

## Slide 27: Loaded Local Supports
These local supports were loaded by the team at SLAC
They are used as the foundation of our system test
We have one coupled ring with RD53a and one L1 half stave

## Slide 28: SLAC System Test Stand/Cold Box

## Slide 29: Coupled Ring and PP0

## Slide 30: Testing with PP0 and RCE @ SLAC
Services FDR 2022
30
9/5/23
The same tests were done at SLAC
  Results are more or less the same
Design changes were made to the quad data flex that improved impedance matching and therefore performance

## Slide 31: Test R0/1 Coupled Ring in QC Box
Serial Power Chain of 10 Quads and 3 Triplets worked quite nicely
Complete Data Transmission Chain with RD53A @ Half Speed
14 Ft of Display port cable ~14dB
~5dB of Loss from Module to Display Port
Modules got to almost -30C, with CO2 at -40C or below
5 quad modules tested with digital/analog/threshold/discBB scans at 5
4 quad modules tested with digital/analog/threshold/discBB scans at -30
No significant changes

## Slide 32: Prototype Barrel
The same process is ongoing for the barrel
All the flexes and PP0 are fabricated assembled, and tested
Integration is ongoing
L1 Data Flex
L1 Power Flex

## Slide 33: Radiation Testing
There are only a few Materials used in the services
  Known to be Radiation Hard
    Kapton
    Copper
    Liquid Crystal Polymer (LCP) (Connectors)
  Tested
    Epoxy (Thinflex, Pyralux HP, etc.)
    Terra Green (Rings and PP0)
    Low Density Polyethylene (LDPE) (Twin-ax)
Many Samples were irradiated
  PP0 samples were received
  Twin-ax samples were received
  Type-0 samples are stuck at irradiation facility
    No visible delamination seen by the staff
  Twin-ax will be discussed in another talk
  PP0(terra green) is below
These dose was 1GRad, Protons
You can see a slight discoloration on the irradiated PP0
PCB did not delaminate

## Slide 34: Quarter Shell Map
Coupled Ring

## Slide 35: Barrel Quarter Shell
DSG-000018000 1.jpg

## Slide 36: L0 and L1 Barrel Flexes

## Slide 37: L0 Barrel Data Flex
The L0 Barrel has only one flavor of data flex and one flavor of data flex
Total Loss is ~ 1dB in the flex

## Slide 38: L0 Barrel Power Flex
The L0 Barrel has only one flavor of data flex and one flavor of power flex
Total power dissipation is ~1.2W
  Budget was 1.26W

## Slide 39: L1 Barrel
Notes: There are four flavors of the L1 data flexes and they are all about 118mm long with a loss of about 0.07dB
We use the IPC standards to calculate the bend radius and validate the results with our mechanical engineering team. The we validate the results with practical tests. Most flexes don’t need test fixtures to be bent and they will hold their shape well enough.

## Slide 40: L1 Power Flex
Notes: There are 2 flavors of the L1 Power flexes and ~1.8 they dissipate about 2.5 watt with a budget of xxx

## Slide 41: Coupled Ring Components
Not Shown
  Quad Module Data Flex
  Triplet Module Data Flex
PP0
Type-0 to PP0 Flex
Rigid Ring
Services FDR 2022
41
9/5/23

## Slide 42: Endcap to Barrel Interface with Type-0 to PP0 Flex
Natural bend not folded
Take up of extra length
Flex in Folded State
Back Flavor
Front Flavor
One Flex contains connections for:
  52 differential pairs
  2 serial power chains
  5 High Voltage Lines
  1 interlocks
  1 Mops Channels
Services FDR 2022
42
9/5/23

## Slide 43: Only 2 flavors
Connectors on different sides
Approx. 315mm
Services FDR 2022
43
9/5/23

## Slide 44: End-cap Integration Model
Coupled Ring Attached to a loaded local support
Quad Module Power Flexes in Red
Triplet Data Flexes in White
Triplet Power T in Grey
Not Shown
  Quad Module Data Flex
  Triplet Power Jumper
Services FDR 2022
44
9/5/23

## Slide 45: R0 Services Details
Triplet power connector
Three flavors of triplet data flexes
One flavor of triplet power to ring flex by adding 2 extra connectors
Triplet power jumper
Due to the clocking of the rigid ring for Type 0 to PPO connections there are 3 different types of disk configurations. To accommodate these configurations we need the flavor of flexes as follows.
Services FDR 2022
45
9/5/23

## Slide 46: Type-0 Triplet Flex Flavors
Configuration 1
Configuration 2
Configuration 3
View from IP
View from HO
Services FDR 2022
46
9/5/23

## Slide 47: End-cap L0
The total power budget for the L0 Triplet serial power chain was quite difficult to meet. However, we believe we have. Our simulations show that we are within budget (0.94W).
The signal loss in the triplet data flex is ~0.325dB

## Slide 48: End Cap L1
The total power budget for the L1 Quad serial power chain was easier to meet. Our simulations show that we are within budget (4.28W).
The signal loss in the quad data flex is ~0.36dB
Loss in the coupled ring is ~1.5dB (0.0044dB/mm)

## Slide 49: Type-0 to PP0
This is quite a dense flex to route
It drives our connectivity
The longest differential pairs here are 330mm long.
This give us a maximum loss of about 2dB
It also means there is no room for length matching which has to be done on the ring services to compensate.
Notes: There are 52 differential pairs in this 6 layer flex PCB. Along with 4 LV channels,5 HV channels, an Interlock, MOPS services, and LP Enable.

## Slide 50: Type-0 to PP0 Folding tool
Our End-cap integration strategy relies heavily on the Type-0 to PP0 flex
We recently changed the connector to z-ray to accommodate the end-cap barrel clearance and resolve potential connectivity issues
This flex carries all of our services
It is quite complicated to design and expensive to make
We use this folding tool to create the different “flavors” which allows us to limit ourselves to two versions of the flex

## Slide 51: Z-Ray Demonstrator
The Z-Ray Demonstrator is designed to do many things
  Demonstrate the use of Z-ray on flex PCBs
  Demonstrate Data Transmission with ITkPixV1
  Demonstrate the mechanical feasibility of long and folded type-0 to PP0 Flex
  Demonstrate the Barrel to End Cap interface
Production is ongoing
This is another example of using a lower cost set of services to validate a more complex design
Services FDR 2022
51
9/5/23

## Slide 52: Other interfaces
Network analyzer & TDR for measuring signal loss and impedance
Oscilloscope for measuring Signal Integrity
RCE board for DAQ @ full speed
SMA to mDP to interface with Network Analyzer, TDR, and Oscilloscope

## Slide 53: QC Testing - Visual Inspection
Type-0 to PP0
BGA Pads on the Type-0 to PP0 Flex
Stereo Microscope
Digital Microscope
Notes: For visual inspection we use microscopes
You can see an image of the BGA pads of the Type0 to PP0 flex (shown below)

## Slide 54: Failure Analysis
The Type-0 to PP0 Flex had some issues
We X-Rayed the flex
  Found a broken track
This is a PCB Fabrication error
We also discovered that many of the BGA joints were disconnected
This is an assembly error
Fixed in two ways, design changes and assembly vendor changes
Tear Drops were expanded, track size was increased, Z-Ray and LPAMs stiffener thickness increased (0.064in 1.63mm total thickness)
Edge of connector
Notes: To verify if the copper was broken in the flex, we removed the connector from the flex and hand tested the flex.
Hand testing without the connector found only 5 errors in the flex.
The edge of the connector is below the bottom edge of the connector, so its not from handling.

## Slide 55: SEM Material Analysis – Coupon Testing

## Slide 56: QC Testing – X-Ray Inspection
Ray Image
Notes: We also are able to use a micro CT tool to Xray the PCBs. You can even look at individual layers.

## Slide 57: Example Test – Reception SEM

## Slide 58: References
Grounding and Shielding Requirements
  https://edms.cern.ch/document/1841188/2
Module ICD
  https://edms.cern.ch/ui/#!master/navigator/document?D:100951222:100951222:subDocs
Quad Hybrid Design
  https://edms.cern.ch/document/2391603/1
Linear Triplet Design
  https://edms.cern.ch/document/2391605/1
ITk Pixel Services Specifications
  https://edms.cern.ch/document/1817540/3

## Slide 59: Quad Ring
Should be One connector

## Slide 60: Intermediate Ring
Should be One connector

## Slide 61: Type-0 Module Interface
Small radius board with separate Quad power flexes

## Slide 62: Triplet Power Jumper Flex
Pixel Workshop
Mechanical Design by Erik Richards

## Slide 63
Strain Relief to be added here

## Slide 64: Triplet Power Flex To Ring
Pixel Workshop
Mechanical Design by Erik Richards

## Slide 65
Strain Relief to be added here
This connector could be rotated differently and there would be minimal impact to our design.