## Slide 1: Innovating Technologies for Liquid Argon Detectors; Behind the Scenes
Kostas Mavrokoridis
k.mavrokoridis@liv.ac.uk
http://hep.ph.liv.ac.uk/ariadne
TIPP, ICFA awards 2023

## Slide 2: Outline
Challenges for the kton scale liquid argon neutrino experiments
Highlights from over a decade of personal key R&D activities and evolution of the ARIADNE program
Recent activities and looking ahead

## Slide 3: A very Exciting Era for LAr Detectors
MicroBooNe
ICARUS T600
SBND -112t
DUNE- ND LAr
DUNE FD 10kt
ProtoDUNEs 750t @CERN
DarkSide-20k
1-ton prototypes
ARIADNE

## Slide 4: Major R&D challenges toward kton scale LAr TPCs
kton scale
LAr TPCs
Ultra-high purity
liquid argon in non
evacuated vessels
Scalable charge readout methods –high granularity tracking & good energy threshold
Very long e- drift length requires very high voltage
Systems 100kV -600 kV
Scalable light readout methods –high granularity tracking & good energy threshold
multichannel DAQ system & Cold electronics
Cryostats & cryogenics

## Slide 5: Establishing a LAr facility
2009
2023
2011
2021
2019
2017
2015
2013
40 L
250 L
500 L gas
1500 L
900 L

## Slide 6: Early activities with 40 L setup
bulk Micromegas in collaboration with CEA Saclay
-Not enough gain in pure argon
CCD imaging integrated S2
Cosmic muon
EMCCD, Successful imaging LAr Muon tracks
Purification and LAr recirculation studies
DOI 10.1088/1748-0221/6/08/P08003
DOI 10.1088/1748-0221/9/02/P02006
DOI 10.1088/1748-0221/10/10/P10004

## Slide 7: The start of ARIADNE program
ERC funding boosted the LAr R&D incredibly
Progressing optical readout and testing tracking capabilities
1500L LAr cryostat

## Slide 8: ARIADNE Detection Principle
ARIADNE has demonstrated light readout as a viable alternative to charge in dual-phase TPC neutrino experiments
Incoming particles ionise LAr and create prompt scintillation light (S1)
Electrons drift towards the extraction grid situated below the liquid level
A THGEM (THick-Gaseous Electron Multiplier) amplifies drift charge (capable of >30 kV/cm in LAr) generating secondary scintillation light (S2)
WLS (Wavelength Shifting) before imaging with Timepix3 camera
ARIADNE (ARgon ImAging DetectioN chambEr)
Cameras
Benefits over previous charge readout techniques:
High resolution
Sensitivity to low energies
Very low noise, decoupled from TPC
Ease of access
Cost efficient

## Slide 9: Technologies in ARIADNE
100kV cryogenically fitted FT
Beam window Cryostat 1500 litres
80 cm field cage
EMCCDs
LASER calibration
Pump and purification
TPX3Cams

## Slide 10: Xmas before shipping to CERN
X-mas in the lab -sent to SPSC confirmation of working detector 31st Dec
Correlated PMT signal
Cosmics
Very first hard task, build 1 ton optical LArTPC and position it at a CERN beamline within 2 years!

## Slide 11: ARIADNE arriving at CERN

## Slide 12: ARIADNE at CERN T9
EMCCD data taking 3 weeks April 2018.
T9 Beamline, East Area, CERN.
Mix of particles: e ±, μ ±, π ±, p±. (0.5 – 8 GeV/c.)
43 cm
35 cm
DOI 10.1088/1748-0221/15/03/P03003

## Slide 13: Going from 2D to 3D: TPX3Cam optical TPC readout
Timepix3 camera installed in place of an EMMCD camera
TPX3 provides simultaneous time-over-threshold (ToT) and time-of-arrival (ToA). Complete (x,y,z,E) event reconstruction using a single device.
Photonis Cricket image intensifier with Hi-QE green photocathode.
VUV Image intensifiers are now also available
ARIADNE results
Coldbox Intensifier
TPB emission
https://www.mdpi.com/2410-390X/4/4/35
https://iopscience.iop.org/article/10.1088/1748-0221/14/06/P06001

## Slide 14: TPX3Cam Optical Readout

## Slide 15: TPX3Cam Optical Readout

## Slide 16: TPX3Cam 3D Cosmics LAr
Continuous streaming, 10 msec slice (playing 1ms jump per frame)
Top View
Side View

## Slide 17
Larger Scale Demonstration at the CERN Neutrino Platform –ARIADNE+
CERN LOI: https://cds.cern.ch/record/2739360
Test optical readout on a scale relevant for DUNE using the existing cold box
Operation Spring 2022

## Slide 18: ARIADNE+: Cryostat Optical Configuration
TPX3 Camera
Assembly (1 x VUV)
Light Readout Plane (LRP)
Cathode
TPX3 Camera
Assembly (3 x visible)
Large scale test of ARIADNE optical readout principle for dual-phase LArTPCs.
Four Timepix3 based cameras, each covering 1m x 1m readout area.
Three cameras detect visible light (wavelength shifter installed above THGEMs)
One camera directly detects VUV.
20-ton Cryostat

## Slide 19: TPX3 Camera System
Timepix 3 Camera
Relay optics
Image intensifier
Objective lens
Visible lenses (f0.95, 10.5 mm)

## Slide 20: 50cm Glass THGEMs
Sixteen 50cm x 50cm glass THGEMs
1.1mm thick,
500μm ID holes,
800μm pitch hexagonal array
Novel Glass THGEMs developed at Liverpool (Patent GB2019563.2)

## Slide 21: Novel G-THGEM Production Method -Going away from FR4 THGEMs
FR4 THGEM with Copper electrodes and holes formed by mechanical drilling.
G-THGEM with ITO electrodes and holes formed by abrasive machining.
Borofloat 33 substrate G-THGEM
Abrasive machining vs drilled holes with chemically etched rims.
G-THGEM: https://www.mdpi.com/2076-3417/11/20/9450

## Slide 22: Light Readout Plane (LRP)
LRP assembly at CERN

## Slide 23: Light Readout Plane
LRP G-THGEMs from underneath

## Slide 24: Commissioning at CERN

## Slide 25: TPX3Cam Cosmics
Visible intensifier: cosmics 30 sec exposure
Energy Calibration
https://arxiv.org/pdf/2301.02530v2.pdf
Visible
VUV

## Slide 26: Using ProtoDUNE dual phase to test optical readouts for Neutrinos and DM; TPX3Cams, X-ARAPUCAs & DarkSide type SiPMs
Next Step
Proposal to SPSC:
TPX Cameras

## Slide 27: Acknowledgments
Core Liverpool team
Many thanks to ICFA committee and community for this award,
it’s a great honor to have this recognition
A. Lowe, A. Roberts, K. Majumdar, B. Philippou, S. Ravinthiran, D. Hollywood, S. Marafico, K. McCormick, G. Stavrakis, J. Vann