## Slide 1
Presenter Name
Date
TIPP School
Simulation workshop on Micro-Pattern Gas Detectors
Maria Teresa Camerlingo and Djunes Janssens
maria.teresa.camerlingo@cern.ch
djunes.janssens@cern.ch
On behalf of the RD51 collaboration
August 2023

## Slide 2: A «good» Detector R&D recipe
Detector design and production
Simulation
Measurements
R&D
RD51 Collaboration working:
WG1 - Technological Aspects and Development of New Detector Structures
WG2 - Common Characterization and Physics Issues
WG3 - Training and Dissemination
WG4 - Simulations and Software Tools
WG5 - MPGD related electronics
WG6 - Production
WG7 - Common Test Facilities

## Slide 3: Introduction
  Garfield++ is an open-source toolkit for the detailed simulation of signals in particle detectors that are based on ionization measurement in gases or semiconductors
  Customised modifications are needed in:
  Field calculations
  Microscopic tracking
  Resistive layers
  Upgrades for gases:
      Excited states
      Ion chemistry
      New mixture with eco-friendly replacements for Greenhouse gases
Garfield: https://garfield.web.cern.ch/garfield/
Garfield++: https://garfieldpp.web.cern.ch/garfieldpp/

## Slide 4: MIGDAL experiment
  Direct dark matter experiments exploit the Migdal effect to extend their sensitivity to low-mass WIMPs, yet the Migdal effect itself has not yet been observed to occur in nuclear scattering.
Images taken from T. Marley’s presentation

## Slide 5: MIGDAL experiment
  Using a GEM based optical time-projection chamber filled with pure CF4 at 50 Torr - for its high scintillation yield and emission spectrum in the visible light – the experiment aims to capture Migdal interactions.
Images taken from T. Marley’s presentation

## Slide 6: MIGDAL experiment
  Detailed simulations were performed in preparation of the experiment to better understand what could be expected.
Images taken from T. Marley’s presentation
electron
NR

## Slide 7: GEM detector
Courtesy of Gabriele Croci and Matteo Alfonsi
  More commonly the readout is based on signal induction, as is the case of the ALICE TPC. Here, a GEM gain multiplication is modelled microscopically.

## Slide 8: MPGD LAB SESSION @TIPP School
In the LAB
  Blabla
TASK 1
Simulation of the number of primaries in ArCO2(93:7)%, which are the involved processes?
  Simulated studies of a MPGD precision tracker
Studies of gain using 55Fe
An essential quantity is the number of primaries

## Slide 9: MPGD LAB SESSION @TIPP School
Charge motion inside a gas volume
TASK 2
Simulation of electron diffusion and drift velocity varying the CO2 fraction and electric field
  Simulated studies of a MPGD precision tracker
Start point
Simplified CO2 cross-section

## Slide 10: MPGD LAB SESSION @TIPP School
Micromegas
To reconstruct the track position of a charged particle in a Micromegas detector.
  Simulated studies of a MPGD precision tracker
TASK 3
𝜇
e-
ion

## Slide 11: See you soon….