## Slide 1
Team 1
Alice McKnight
Nkosiphendule Njara
Anza-Tshilidzi Mulaudzi
Instrumentation School in Particle, Nuclear and Medical Physics.
iThemba Labs 2023
iThemba Labs Instrumentation School 2023
1

## Slide 2
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
2
Main goal:
Optimise the resolution of a single silicon sensor of the CMS type.
Vary various parameters i.e. digitisation, rotation, magnetic field.
The Allpix2 framework:
A generic, open-source software framework for the simulation of silicon pixel detectors. Its goal is to ease the implementation of detailed simulations for both single detectors and more complex setups such as beam telescopes, from incident radiation to the digitised detector response.
It consists of four main stages of the simulation from a particle crossing a silicon sensor to the final detector response: Interaction, Propagation, Assignment to readout channel, Front-end response.

## Slide 3
Exercise 1: Allpix2
iThemba Labs Instrumentation School 2023
3
Interaction:
In this very first stage, an incident particle interacts with the detector material, depositing energy in the material. This energy loss is converted to electron-hole pairs in silicon.
Propagation:
After electrons and holes have been created, they move in the silicon lattice owing to drift and diffusion processes. In the simulation, a (user-defined) electric field inside the active sensor volume is used to guide the charge carriers towards the collection electrodes.
Assignment to readout channel:
The signal formed by the movement of charge carriers is processed by the front-end electronics. In the simulation, the signal has to be assigned to a front-end channel, i.e. a pixel collection electrode, before this takes place.
Front-end response:
the behaviour of the readout circuitry is simulated: The charge assigned to individual pixels is processed by the amplifier and discriminator in this pixel cell, digitizing the signal with a configurable conversion from charge carriers to charge-to-digital converter

## Slide 4
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
4
Conditions for simulation:
Magnetic field = 8.3T in x-axis
Rotation angle = 0 deg (run 1) and 27 deg (run 2)
Particle = electron
Source energy = 5 GeV
Voltage = -150 V
Depletion voltage = -50 V
temperature = 293K
Resolution: 1(run 1) and 8 (run 2)

## Slide 5
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
5
Run 1:

## Slide 6
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
6
Run 2:

## Slide 7
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
7
Run 1
Run 2

## Slide 8
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
8
Run 1
Run 2

## Slide 9
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
9
Run 1
Run 2

## Slide 10
Exercise 1 – Resolution of a silicon pixel detector
iThemba Labs Instrumentation School 2023
10

## Slide 11
Exercise 2 – Data Acquisition using VMEBus
Learning achievements:
Read/Write data in A32/D32 mode
Single Cycles vs Block transfers
Safe vs Fast modes
Master, Slave and Analyzer
iThemba Labs Instrumentation School 2023
11

## Slide 12
Exercise 4 – Micro Pattern Gas Detector
iThemba Labs Instrumentation School 2023
12
ArCO2 (70:30)%.
Two processes occur namely, Auger Effect and Photo electric effect.
Large peak due to Auger Effect where 2 electrons are liberated, giving rise to more charge collection.
Smaller peak as a result of Photoelectric effect, liberating only 1 electron.

## Slide 13
Exercise 4 – Micro Pattern Gas Detector
iThemba Labs Instrumentation School 2023
13
Incoming signal from charge collection:
Electric field in xy plane due to wire mesh and surrounding electrodes:
Movement of electrons (yellow) and ions (red)

## Slide 14
Exercise 5 – Calorimetry Silicon Tungsten
iThemba Labs Instrumentation School 2023
14
Low voltage power supply
High voltage power supply
PCB containing 16 chips reading out the 1024 silicon cells

## Slide 15
Exercise 5 – Calorimetry Silicon Tungsten
iThemba Labs Instrumentation School 2023
15

## Slide 16
Exercise 5 – Calorimetry Silicon Tungsten
iThemba Labs Instrumentation School 2023
16
Radium Source:
Iron-55 Source:

## Slide 17
Exercise 5 – Calorimetry Silicon Tungsten
iThemba Labs Instrumentation School 2023
17
:
Decays via electron capture
p + e− → n + νe
Daughter nucleus 55Mn de-excites releasing a 126 keV photon
126 keV should interact with silicon, but…
Photoelectric effect
(at low energies)
Silicon: Z = 14
Low intensity source…
Low statistics…
Iron-55 Decay Scheme:
Table of Isotopes:

## Slide 18
Thank you !