## Slide 1: Data Processing for the ALICE at the LHC
High-performance Signal and Data Processing
Wits – 26-31 January 2014

## Slide 2: Contents
Physics Motivation
heavy-ion physics and QGP
hard and soft probes
Present ALICE Setup
detectors
triggering
ALICE upgrade
ITS, TPC upgrades
challenges
O2 project

## Slide 3: Quark-Gluon Plasma
Compression
reduce distance between nucleons
Heating
thermally create pions
fill space between nucleons
hadrons overlap
quarks roam freely over large volume (deconfinement)
Quark-Gluon Plasma

## Slide 4: QGP in the Laboratory
raw material: nuclei
  density: 2×1017 kg/m3 ≈ 0.1 GeV/(fm3 c2)
kinetic energy
  up to E=2.76 TeV per nucleon
  about 3000 times rest energy (938 MeV)
collision: 208Pb + 208Pb @ √sNN=2.76 TeV
  Etotal = 1.15 PeV ≈ 0.2 mJ
  typ. volume: (10 fm)3
  energy density: TeV/fm3 ≈ 1038 J/m3
  typ. time: 10 fm/c ≈ 10-22s

## Slide 6: Bulk Properties
global observables of particle production
  hadron species
  anisotropy and momentum distribution
direct access to thermodynamic properties
  freeze-out temperature
  baryo-chemical potential at freeze-out
  pressure gradients and hydro-dynamic flow

## Slide 7: Statistical Model
For any conserved quantum number exists a chemical
potential μ, conservation laws give boundary conditions:
Baryon number:
Strangeness:
Charge:
Leaving two free
parameters:
+ : fermions - : bosons
Assumption: thermal production of all hadrons in macro-canonical ensemble
→ hadron abundances are fixed by partition function

## Slide 8: Statistical Model in ALICE
Fit particle ratios to extract freeze-out temperature
T=152 MeV 2 trillion K
µB = 1 MeV (fixed)
exclude protons to improve fit
Consistent with phase transition around 150-160 MeV

## Slide 9: Phase Diagram of Nuclear Matter
increasing T for small √sNN
const T≈160 MeV for √sNN>10GeV
consistent with lattice QCD
  crossover phase transition at SPS,RHIC energies
  1st order phase transition, critial point predicted search ongoing
baryon free region at mid-rapidity

## Slide 10: Bulk Properties – Data Sets
abundant probes
  1000s of pions, 100s of kaons, protons… per collision
small data sets required
  first analyses with few hours worth of data
typical triggers:
  minimum-bias (MB): simple interaction trigger
  centrality trigger: select e.g. 10% collisions with smallest impact parameters

## Slide 11: Hard Probes
created in early hard N-N scatterings
typical examples:
  jets
  high-pT prompt photons
  W/Z bosons
penetrating probes for the QGP (jets) or reference (photons, W/Z)

## Slide 12: Jets in Heavy-Ion Collisions
hard production process
  well understood in pQCD
propagation in medium
  gluon-Bremsstrahlung
  collisions with partons
  energy loss – „jet quenching“
jet modifications carry information about parton-medium interaction → probe of the medium

## Slide 13: Single Particle Spectra
Jet Quenching:
shift from high to low jet energies
fewer hard jet fragments
suppression of high-pT single particle spectra
  strongest for central Pb-Pb
  absent in p-Pb
Phys Rev Lett 110, 082302

## Slide 14: Hard Probes - Requirements
rare probes
  1 jet > 100 GeV in 106 MB Pb-Pb events
  1 direct photon > 10 GeV in 104 events
easy to trigger
  jets: energy deposition in large calorimeter area
  photons: large energy in few calorimeter cells
  muons: penetration of absorbers

## Slide 15: “Semi-hard” Observables
observables between bulk and hard probes
examples
  heavy quarks (c,b)
    hydro-dynamics
    charm quark energy loss / jet quenching
    J/ψ suppression
  thermal photons at low-pT

## Slide 16: D-Mesons
test charm quark transport in the QGP
mass dependence of jet quenching
hydrodynamics and thermalization
difficult reconstruction
secondary vertex and invariant mass
e.g. D+ → K-π+π+
JHEP 1207 (2012) 191

## Slide 17: Identified Charm RAA
  reconstructed D-mesons
  D0, D+, D*
  semi-leptonic decays
  b,c → e + X
  b,c → μ + X
  suppression of heavy flavor slightly less than for light hadrons

## Slide 18: “Semi-Hard” Observables - Requirements
rarely produced
  large event samples required
no clear trigger signal
  decay into many soft particles
  indistinguishable from background at trigger level
  online event selection not possible
focus of ALICE upgrade program

## Slide 20: ALICE / LHC Heavy-Ion Running
1 month heavy-ion running per year
  Pb-Pb @ 2.76 (5.5) TeV – up to 8 kHz
  p-Pb @ 5.02 (8) TeV – 100-200 kHz
  other systems under discussion (Ar-Ar)
10 months pp running per year
  reduced luminosity at ALICE (100-200 kHz)
  mainly as reference for HI data

## Slide 21: Time Projection Chamber
largest TPC ever built
L=5m, d=5m, V=88m3
570 000 readout pads
1 event = up to 1000 10-bit samples @ 5.66 MHz
tdrift ≈ 90 μs
max event rate 3.5 kHz
reconstruction and identification of charged particles with up to 160 space points
Notes: note: gating grid: needs to be closed between events – space charge

## Slide 23: TPC – Particle Identification
negative particles → no nuclear fragments from detector
separation of anti-helium 3 / 4 with TOF

## Slide 24: TPC – Event Size and Data Rate
TPC is largest data source
limiting factor for Pb-Pb (ZS: 1 GB/s @ 50 Hz)
→ record cluster data
cluster reco in FPGAs in High-Level Trigger
discard raw data
increase max event rate to 400 Hz (still at 1GB/s)
rate limit in pp ≈ 3.5 kHz (gating grid)
Data Format | Event Size (MByte)
Raw Data | 700
Zero Suppression | 20
Cluster Data | ~3
HLT Pb-Pb 2011

## Slide 25: ALICE Trigger Scheme
Level-0 Trigger | t = 1.2 μs | T0, V0, TOF | interaction, centrality
 | Rmax ≈ 100 kHz |  | 
Level-1 Trigger | t = 6.5 μs | TRD PHOS,EMCAL | high-pT hadrons, photons, jets, electrons
Level-2 Trigger | t = 88 μs |  | 
 | Rmax ≈ 1 kHz |  | 
High-Level Trigger | BWmax ≈ 1GB/s | all detectors | arbitrary observables
1 μs
10 μs
100 μs
Collision
Level-2
Level-0
Level-1
Pretrigger
high levels: detailed information, precise decisions
low Levels: high event rates – 10x statistics per level
LHC: 8 kHz Pb-Pb
100 kHz pp @ ALICE

## Slide 26: ALICE Transition Radiation Detector
electron identification
  using transition radiation and ionization
  pion efficiency < 1%, with electron efficiency > 90%
Level-1 trigger
  for electrons, high-pT hadrons
  6.5 μs processing
  requires tracking and PID
  implemented in ASICs and FPGAs
Notes: Spurrekonstuktion
Elektronidentifikation
Trigger
6 Ebenen, 18 Supermodule, 540 Kammern
Radiator + MWPC mit Drift

## Slide 27: TRD Electron Trigger
Front-End Electronics
70000 ASICs
tracklet reconstruction
tracklet particle ID
Global Tracking Unit
109 FPGAs
track reco using tracklets
combined PID
trigger decision
Triggers in p-Pb run 2013
high-pT electrons (high eff.)
low-pT electrons (less eff.)
jets

## Slide 28: ALICE Long Term Plan
Main goal: inspect 100x more events
focus on unique selling points:
  thermalisation and energy loss of heavy quarks (c,b)
  low-momentum quarkonium dissociation and regeneration
  photons and low mass dileptons
  anti- and hyper-nuclei
complementary to ATLAS and CMS
LHC: high luminosity running after 2018 “HL-LHC”
Pb-Pb: max. interaction rate 8 kHz → 50 kHz
CERN-LHCC-2012-012

## Slide 29: New ITS
higher readout rate
current: 1 kHz
planned:
  50 kHz Pb-Pb
  several 100 kHz pp
  triggered or continuous RO
smaller material budget
reduced BG from photon conversions
better vertex resolution
closer to beam line
improve D-meson measurements

## Slide 30: TPC Rate Limitations
gating grid
  open during drift time to allow electrons into MWPC
  closed afterwards to prevent ion back-flow
  limits readout rate to 3.5 kHz
opening GG permanently not possible
  ion back flow creates large space charge
  space point distortions up to 1 m – not tolerable

## Slide 31: TPC Upgrade
replace MWPCs with GEMs
no gating
continuous operation
small ion back-flow
continuous readout
sample at 10 MHz (7 TB/s)
ship zero-suppressed raw data stream to DAQ (1 TB/s)
continuous stream – no “events” in FEE
R&D ongoing
promising test run 2012/13
investigation of gain stability

## Slide 32: Challenge: Data Volume
Massive data volume reduction needed
Only option is by online processing
Detector | Event Size | Bandwidth @50 kHz Pb-Pb (GByte/s)
 | After Zero Suppression (MByte) | 
TPC | 20.0 | 1000
TRD | 1.6 | 81.5
ITS | 0.8 | 40
Others | 0.5 | 25
Total | 22.9 | 1146.5

## Slide 33: TPC Data Volume Reduction
TPC data volume reduction by online event reconstruction
Discarding original raw data
In production from the 2011 Pb-Pb run
some optimization still needed
 | Data Format | Data Reduction Factor | Event Size (MByte)
 | Raw Data | 1 | 700
FEE | Zero Suppression | 35 | 20
HLT | Clustering & Compression | 5-7 | ~3
 | Remove clusters not associated to relevant tracks | 2 | 1.5
 | Data format optimization | 2-3 | <1
HLT Pb-Pb 2011

## Slide 34: Total Data Volume
LHC luminosity variation during fill and efficiency taken into account for average output to computing center
Detector | Input to Online System (GByte/s) | Peak Output to Local Data Storage (GByte/s) | Avg. Output to Computing Center (GByte/s)
TPC | 1000 | 50.0 | 8.0
TRD | 81.5 | 10.0 | 1.6
ITS | 40 | 10.0 | 1.6
Others | 25 | 12.5 | 2.0
Total | 1146.5 | 82.5 | 13.2

## Slide 35: O2 Project
optimization and upgrade of all computing efforts necessary:
DAQ (data acquisition): handle data volume
offline: reconstruction and data analysis
HLT (High-Level Trigger): online reconstruction and data reduction
common effort: Online-Offline project
close collaboration
15 computing working groups (CWG): overall system, computing platforms, hardware, reconstruction, calibration, software lifecycle…

## Slide 36: Dataflow Model

## Slide 37: Dataflow Model
detector local processing
data reduction, e.g. cluster finding
time slicing → data from consecutive 100-1000 events
first calibration procedures

## Slide 38: Dataflow Model
global processing
full online reconstruction
further data reduction
  using track info → keep only clusters on tracks
  keep sufficient information for re-processing with improved calibration
requires and provides online calibration

## Slide 39: Dataflow Model
offline processing
improved reconstruction passes with better calibration
100x more events → tuning necessary
offline analysis
scaling to 100x more events?

## Slide 40: O2 Hardware System
2 x 10 or 40 Gb/s
FLP
10 Gb/s
FLP
FLP
ITS
TRD
Muon
FTP
L0 L1
FLP
EMC
FLP
TPC
FLP
FLP
TOF
FLP
PHO
Trigger Detectors
~ 2500 links in total
~ 250 FLPs
First Level Processors
EPN
EPN
Data Storage
Data Storage
EPN
EPN
Storage
Network
Farm
Network
10 Gb/s
~ 1250 EPNs
Event Processing Nodes

## Slide 41: Summary
Heavy-Ion Physics
bulk and hard probes to study deconfined state of nuclear matter – QGP
Present ALICE Setup
dedicated heavy-ion experiment
excellent PID capabilities
event based readout
trigger for jets, electrons, muons
ALICE Upgrade
100 times more statistics - recording of all events
major detector upgrades: TPC and ITS
must be accompanied my new online & offline computing → O2 upgrade