## Slide 1: Perspectives in Boron Neutron Capture Therapy (BNCT) of cancer
Ignacio Porras Departamento de Física Atómica, Molecular y Nuclear Universidad de Granada, Granada, Spain.
E-mail: porras@ugr.es
www.isnct.net
President: Ignacio Porras
Secretary: Silva Bortolussi

## Slide 2
Sponsors of our research
Boron Nanostructures for BNCT. Research Project 20F12/41 (2012),
New production routes for medical radioisotopes. Project P-BS-64 (2014)
Internacional Excellence Campus of the University of Granada
Innovative Low energy neutron capture therapies.
Excelence Research Proyect P11-FQM-8229 (2012-2016).
Computer Monte Carlo Simulations.
FIS2015-69941-C2-1-P (2016-2018).
Cofounds a PhD student at ILL Grenoble
Founding a University Chair: Neutrons for Medicine
Study and design of new neutron capture treatments. Spanish Society Against Cancer (AECC) Singular Projects 2016 (2016-2019).
Grant for testing new boron compounds (2018-2019)
Donation for research (2019)

## Slide 3
Ignacio Porras, Javier Praena, Fernando Arias de Saavedra,
María Pedrosa, Pablo Torres-Sánchez, Nataliya Ramos-Chernenko
Departamento de Física Atómica, Molecular y Nuclear, Universidad de Granada.
M. Carmen Ruiz-Ruiz, M. José Ruiz-Magaña
Departamento de Bioquímica y Biología Molecular III e Inmunobiología
Centro de Investigación Biomédica, Granada.
Our team and collaborators
José Expósito
UCG Oncología, H.U. Virgen de las Nieves de Granada, Junta de Andalucía
José M. Llamas, Ángel Ramírez, Antonio Rodríguez
UGC Medicina Nuclear. H.U. Virgen de las Nieves de Granada, Junta de Andalucía
Juan L. Osorio, José C. Ramírez, Clara Jover, Eduard Massana
Servicio de Radiofísica y Protección Radiológica. H.U. Virgen de las Nieves de Granada, Junta de Andalucía
The Neutron Time of Flight
(n_TOF) Collaboration
CERN, Geneva, Switzerland
Ulli Köster, Torsten Soldner, Trevor Forsyth
NPP and Life Sciences groups
Institute Laue-Langevin, Grenoble, France

## Slide 4
Outline
Introduction to BNCT
Conclusions
Accelerator-based neutron sources for BNCT
Research problems

## Slide 5
Introduction to Boron Neutron Capture Therapy (BNCT)

## Slide 6
BNCT treatment starts with a 2 hour intravenous boron compound infusion
Boron is accumulating in the cancer cells
Targeted neutron irradiation is given according to the Monte Carlo dose plan
10B[n,]7Li
rection
neutron
Alpha particle
7Li recoil nucleus
10B -nucleus
The boron atoms capture neutrons, leading to nuclear reaction emitting alpha and lithium recoil particles that cause extensive radiation damage in the cancer cells
~2x20min
(Courtesy of L. Kankaanranta & M. Kortesniemi, HUCH)
BNCT: Effective Treatment In One Day
Notes: 6

## Slide 7
Key: diferent depth dose profiles

## Slide 8
Pioneers of BNCT
Gordon L. Locher
Biological effects and therapeutic
possibilities of neutrons.
Am.J. Roentgen. Radium Ther. 36, 1 (1936).
William H. Sweet
First BNCT clinical trials
MGH + BNL, USA
Hiroshi Hatanaka
Developed BNCT programme in Japan

## Slide 9
Early clinical trials in the 50’s for brain tumors
Brookhaven Medical Research Reactor

## Slide 10
Modern BNCT (from 1990)
Phase II clinical trials
Epithermal neutron beams from reactors
- Kyoto University Research Reactor
- FiR1 in Helsinki
- THOR in Taiwan
… and others
Epithermal: 1 eV to 10 keV
More selective compound (BPA)
Application to Brain tumors, Head & Neck local recurrent
Other applications:
- melanoma
- liver metastasis (extracorporeal)
- other tumors are in study
Treatment Room at FiR1 Research Reactor, Helsinki

## Slide 11: JRR-4 Japan Atomic Energy Agency (JAEA) at Tokai
Developed for the nuclear-powered ship “Mutsu”
First critical state 1965
Remodeling for BNCT 1998
1st human treatment Aug 26, 1999

## Slide 12
Modern clinical trials under protocol (reactors)
Medical institution | Neutron source | Glioblastoma | Head & Neck
Osaka Medical College, Japan & Kyoto U., Japan | Kyoto University Research reactor (KURR) | 50 p. (1998-2008) | 94 p. (2001-2008)
University of Tsukuba, Japan | JRR-4 reactor | 24 p. (2002-2007) | 30 p. (2003-2008)
University of Tokushima, Japan | JRR-4 or KURR | 23 p. (1998-2008) | 
Harvard Medical School, USA | MIT Research Reactor | 28 p. (1998-2003) | 
Helsinki Univ. Central Hospital, Finland | FiR-1 reactor | 52 p. (1999-2008) | 35 p. (2003-2011)
Universität Essen, Germany | High flux reactor JRC Petten | 27 p. (1997-2006) | 
Nyköping Hospital, Sweden | R2-0 Studsvik Reactor | 43 p. (2001-2005) | 
Taipei Veteran General Hospital, Taiwan | THOR research reactor |  | 10 p. (2010-2011)

## Slide 13
Clinical results for Glioblastoma - Finland
Joensuu et al. Journal of Neuro-Oncology, 2003.

## Slide 14
Clinical results for Glioblastoma - Japan
Barth et al. Radiation Oncology 2012, 7:146

## Slide 15
Shin-Ichi Miyatake, Osaka Medical Center
F-BPA-PET
：bevacizumab

## Slide 16
Shin-Ichi Miyatake, Osaka Medical Center

## Slide 17: 11-year survivor no neurological deficit
Tetsuya Yamamoto, Neurosurgery Dpt.,
Yohohama City University,
Japan

## Slide 18
BNCT of Explanted Liver at Triga reactor
explanted
washed and
refrigerated
Liver metastases from colon carcinoma
irradiated in the thermal column
destroyed metastases
Triga Mark II reactor
Notes: In Pavia we have a long tradition on BNCT
We started with the Taormina project dedicated to BNCT of the spread liver metastases
After the BPA infusion the explanted liver was irradiated in the T.C. of the Triga Mark II reactor
All metasatases where very selectively destroyed

## Slide 19
BPA infusion and Boron concentration measurement
BPA administered at a dose of 300 mg/Kg
body weight,
during surgery, through a colic vein.
To measure Boron concentration
some biopsies were taken
both from healthy and tumour
1h/2h after BPA infusion.
neutron autoradiography image
histological image
Normal hepatocytes
necrotic areas
tumor cells
Neutron autoradiography
 | FIRST PATIENT | SECOND PAT.
TUMOR (ppm) | 47  2 | 45  5
LIVER (ppm) | 8  1 | 8  1
TUMOR/LIVER | 5.9 | 5.6
Alpha spectrometry

## Slide 20
Clinical results for Head and Neck
Kouri et al. Radiotherapy and Oncology, 2004.

## Slide 21
Clinical results for Head and Neck
Kouri et al. Radiotherapy and Oncology, 2004.

## Slide 22
Clinical results for Head and Neck
Kouri et al. Radiotherapy and Oncology, 2004.

## Slide 23
Survival plots
NUPECC Report: Nuclear Physics for Medicine (2014)

## Slide 24
IAEA recognizes BNCT progress

## Slide 25
Accelerator-based neutron sources (ABNS)

## Slide 26
Complex dosimetry: main dose contributions
Fast (and epithermal) neutrons (elastic collisions)
Gamma emission
(hydrogen capture)
1H(nγ) 2H
Thermal neutrons
(nitrogen capture)
Boron capture
1H(n,n’)p
14N(n,p) 14C
10B(n,α) 7Li
Physical Dose:
Dose components

## Slide 27
Range of “useful” neutrons for deep seated tumor: epithermal (1 eV to 20 keV)
Optimal neutrons are at 2 keV
What is the optimal neutron energy for BNCT?
Monoenergetic neutrons: plot of weighted dose ratio tumor/max normal tissue

## Slide 28
Accelerator-based compact neutron sources for BNCT
Requires low energy but high intensity (tens of mA) particle accelerator, now available!
Will allow in-hospital facilities
More patients, more cases…

## Slide 29
Reactions considered
Reactions proposed

## Slide 30
Current projects
Institute | Accelerator | Beam energy | Intensity | Reaction | Max. n energy
Kyoto Univ, Japan (in clinical trials) | Cyclotron | 30 MeV | 1 mA | 9Be(p,n) | 28 MeV
Helsinki Univ. Cent. Hospital, Finland | Electrostatic (Hyperion) | 2.6 MeV | 30 mA | 7Li(p,n) | 0.89 MeV
Budker Institute, Novosibirsk, Russia | Vacuum insulated Tandem | 2 MeV | 2 mA | 7,Li(p,n) | 0.23 MeV
IPPE Obninsk, Russia | Cascade generator KG-2.5 | 2.3 MeV | 3 mA | 7Li(p,n) | 0.57 MeV
Birmingham Univ., UK | Electrostatic (Dynamitron) | 2.8 MeV | 1 mA | 7Li(p,n) | 1.1 MeV
Tsukuba Univ., Japan | RFQ-DTL a | 8 MeV | 10 mA | 9Be(p,n) | 6.1 MeV
CNEA Bs. As., Argentina | Tandem Electrost. Quadrupole | 1.4 MeV 2.5 MeV | 30 mA 30 mA | 9Be(d,n) 7Li(p,n) | 5.7 MeV 0.79 MeV
INFN, Italia | RFQ a | 5 MeV | 50 mA | 9Be(p,n) | 3.1 MeV
SOREQ, Israel | RFQ-DTL a | 4 MeV | 2 mA | 7Li(p,n) | 2.3 MeV
LBNL, USA | Electrostatic | 2.5 MeV | 50 mA | 7Li(p,n) | 0.79 MeV
National Cancer Center, Japan | RFQ a | 2.5 MeV | 20 mA | 7Li(p,n) | 0.79 MeV
Xiamen Humanity Hospital, China | Electrostatic (VITA) | 2.5 MeV | 10 mA | 7Li(p,n) | 0.79 MeV
Nagoya Univ., Japan | Electrostatic (Dynamitron) | 2.8 MeV | 15 mA | 7Li(p,n) | 1.1 MeV
Gachon Univ. Gil Med. Center, S.Korea | RFQ-DTL a | 10 MeV | 8 mA | 9Be(p,n) | 8.1 MeV
Southern Tohoku Hosp, Fukushima, JP | Cyclotron | 30 MeV | 1 mA | 9Be(p,n) | 28 MeV
Granada Univ., Spain | Electrostatic (Hyperion) | 2.1 MeV | 30 mA | 7Li(p,n) | 0.35 MeV
a RFQ stands for Radio Frequency Quadrupole and DTL for Drift Tube Linac.

## Slide 31
Boost of BNCT in new AB-facilities
The number of projects for future BNCT ABNS is larger than the number of facilities where BNCT has been applied clinically in all history.
Most in-hospital facilities
SOUTH KOREA: Incheon
ARGENTINA:
CNEA
(Buenos Aires)
JAPAN:
C-BENS (Kyoto-Osaka)
i-BNCT (Tsukuba)
Tokio
Nagoya
Fukushima
Kanagawa
RUSSIA: Obninsk, Novosibirsk
FINLAND: Helsinki
UK: Birmingham
ITALY: Pavia
SPAIN: Granada
ISRAEL: Soreq
CHINA: Xiamen
USA:
LLNL

## Slide 32
Japan projects
Japan is the world leader in BNCT
The first and only ABNS doing clinical trials is C-BENS at Kyoto
Six different projects for BNCT with different accelerators in development
New treatments foreseen: pancreatic cancer, other disseminated tumors
Project at National Cancer Center, Tokio

## Slide 33
Finnish project
New facility in Finland expected for the end of 2019 at Helsinki University Central Hospital
Electrostatic accelerator of Neutron Therapeutics
Only facility in Europe expected soon

## Slide 34
LINAC based A-BNCT center in Korea
Building : 35.3 x 21.8 m2 with shielding
Utility : Electricity, Cooling, Air Cond.
Accelerator Room
Treatment Room #1
Treatment Room #2
Treatment Room #3
(BNCT Lab.)
Treatment Preparation Room
Control
Room
Injection
Room
Radiation
Safety
Management
Entrance
Emergency Exit
Post-treatment
Moderator
Assembly
(Inside)
Reception
BNCT Lab
Dosimetry Lab
Be Target & Moderator Assembly (BSA)
Proton Injector
RFQ
DTL
BTL
Control Room
LINAC based A-BNCT center in Korea

## Slide 35
Elements of ABNS
The spectrum can also be improved
BSA (Beam Shape
Assembly): moderator (MgF2, AlF, etc.), reflector (Bi, Pb), filter and shielding (Li-poly, LiF)
Neutron producing target

## Slide 36
International Society for Neutron Capture Therapy
ISNCT: Involves multidisciplinary researchers in the field collaborate in a spirit of close collaboration
Promotes the future development of BNCT
www.isnct.net
President: Ignacio Porras
Vice-President: Akira Matsumura
Gen. Secretary: Silva Bortolussi

## Slide 37
Open research problems in BNCT

## Slide 38
The boron carrier

## Slide 39
boron-rich dendrimers with porphyrin nucleus:
J. Cabrera et al., Inorg. Chem., 2015, 54 (10), 5021–5031
10 atoms of boron in each
carborane cage
Until now:
BPA
BSH
Nanoparticles:
boronophenylalanine
sodium borocaptate
Nanoparticles

## Slide 40
Functionalized liposomes
BNCT will probably benefit from the important advances in nanobiotechnology for tumor targeting
Hiroyuki Nakamura, Future Med Chem. 2013, 5(6):715-30.

## Slide 41
The treatment planning

## Slide 42
Sources of uncertaintites
Physical dose > Cross section of processes not well known – Nuclear data (n_tof at CERN)
Equivalent (biological) dose > requires RBE factors not well known – Radiobiological data from ILL

## Slide 43
Most important processes contributing to dose in brain (healthy tissue)
44

## Slide 44
Guber (2002)
45
Wagemans (2001)
Koehler (1993)
14N(n,p)
Cross section measurements at n_TOF
35Cl(n,g)

## Slide 45
14N(n,p) cross section measured at n_TOF-EAR2
44
(preliminary)
Measured with Micromegas and silicon detectors
in 2018

## Slide 46
35Cl(n,γ) cross section measured at n_TOF-EAR1
44
Measured at n_TOF in 2018
- 4 C6D6 detectors (n insensitive)

## Slide 47
Physical Dose:
weighting factors currently used (Coderre et al.)
(tumour) (Healthy tissue)
weighting factors currently used (Coderre et al.)
To introduce relative different biological effect:
Weighting factors (RBE).
Weighted dose:
Biological dose in BNCT
A major source of uncertainty:
could not be separated (assumed the same)
In current measurements of , gamma dose is dominating -> loss of precision
should be measured in a pure thermal beam (or equivalent, like PF1b at ILL)
depends on facility, requires
assumed 1, should be confirmed

## Slide 48
PF1B - cold neutron beam facility
PF1B is dedicated to the particle and nuclear physics experiments. It provides an intense polarized or unpolarized cold neutron beam.
Bent guide: avoid contamination by gammas and fast neutrons.
Additional collimation after guide exit to minimize lateral captures
2 cm Ø beam at Experimental Zone
Capture flux 2 109 n/(s cm2)
-
- low value
Thermal and boron factor: determination at ILL

## Slide 49
1. Fill quartz cuvettes with cell culture and let them attach to one side
2. Place the cuvette on the setup at Pf1b and irradiate. (2,4 Gy/h)
3. Take the irradiated cuvettes, recover the cells and prepare for clonogenicity
4. After 8 days, analyse the clonogenicity assays:
0 Gy
4 Gy
5. Results:
Chart: A375 survival study (preliminary results)
| 0 min | 10 min | 20 min | 40 min | 120 min
 | 134.6667 | 133.3333 | 105.3333 | 34 | 7.3333
ILL irradiation procedure

## Slide 50
We need a lot of samples
The samples need to be prepared in a level P2 lab
P2 lab inside the ILL7 (instruments hall)
NEW!
A new class 2 Bio Lab was built for this purpose

## Slide 51
A375 (melanoma cells) in quartz cuvettes
= 0.187 Gy-1 , = 0.035 Gy-2
First results: thermal factor
= 1.327 ± 0.049 Gy-1
Survival (%) | (Gy) | (Gy) | (RBE)
100 - limit | Limit → 0 | Limit → 0 | 7.096 ()
75 | 0.217 | 1.247 | 5.753
50 | 0.522 | 2.519 | 4.823
37 | 0.749 | 3.290 | 4.392
25 | 1.045 | 4.166 | 3.987
10 | 1.735 | 5.868 | 3.382
5 | 2.258 | 6.958 | 3.082
1 | 3.470 | 9.106 | 2.624
Survival (%) |  |  | 
100 - limit | Limit → 0 | Limit → 0 | 
75 | 0.217 | 1.247 | 5.753
50 | 0.522 | 2.519 | 4.823
37 | 0.749 | 3.290 | 4.392
25 | 1.045 | 4.166 | 3.987
10 | 1.735 | 5.868 | 3.382
5 | 2.258 | 6.958 | 3.082
1 | 3.470 | 9.106 | 2.624
We are in a experimental campaign of measuring these weighting factors for different cell lines of both tumor and normal cells (ILL-PhD fellowship of Maria Pedrosa)

## Slide 52
Conclusions

## Slide 53
Conclusions
BNCT is the “last line” in the fight of cancer (provides a hope when everything else fails)
Every new application tried has led to a great success
Accelerator-based neutron sources will allow:
  Increase statistics (randomized clinical trials)
  Improved treatments
  Increased visibility (more public and private funding)
Great potential (translation of research results)

## Slide 54: Thank you for your attention!
19th International Conference on Neutron Capture Therapy
Granada (Spain),
13-18 September 2020
E-mail porras@ugr.es for being included in the info list